## Slide 1: FIRO National Screening Updates: National Precipitation Forecast Skill Assessment
Jason M. Cordeira, Rachel R. Weihs, and Emily A. Slinskey
Center for Western Weather and Water Extremes
UCSD Scripps Institution of Oceanography
Tuesday, 5 August 2025
FIRO Workshop

## Slide 2
Forecast Informed Reservoir Operations (FIRO)
Top of Normal “Conservation” Pool
FIRO Pool: 11,600 ac-ft
FIRO Pool:
Flexibility depends on skillful streamflow
and QPF Forecasts
Guerneville
flood prone
~1–3 days travel time
Lake Mendocino
Recall FIRO allowed retention of an extra 11,600 acre-feet at Lake Mendocino during Dec 2022–Jan 2023.

## Slide 3
Leveraging enhanced skill to screen for potential FIRO viability
Lead Time (e.g., 1–14 days)
Precipitation Forecast Skill
#2
Candidate Reservoir Watershed #1
Candidate Reservoir Watershed #2
Skill threshold
FIRO
Lead-time
Requirement (i.e., release + travel time)
#1
Potentially viable for FIRO?
Viability is influenced by whether skill is high enough at a given lead-time requirement.
Cordeira et al. (2025)

## Slide 4
Based on GEFS-R and PRISM data for 2000–2019
Days 1–3 [F12–F84] Critical Success Index
US States
HUC-8 Boundaries
USACE Sites (from National Inventory of Dams)
A National Precipitation Forecast Skill Assessment for Screening
Based on GEFS-R vs PRISM data for 2000–2019
Days 1–3 QPF Skill (CSI) for Top-5% Wettest Periods (2000–19)
Leading Hypotheses:
Highest skill over West anchored by terrain and ARs.
Higher skill also over New England and Mid-Atlantic influenced by ARs and Nor’easters (synoptic-scale precip).
Lower skill over Central and Southeast influenced by convection and tropical processes (with some exceptions; e.g., along the Appalachians, lower Ohio).
Results summarized in a recent article:
Cordeira, J. M., F. M. Ralph, C. Talbot, J. Forbis, D. R. Novak, J. A. Nelson, K. Mahoney, R. Weihs, E. Slinskey, and L. Delle Monache (2025). A summary of U.S. watershed precipitation forecast skill and the national Forecast Informed Reservoir Operations Expansion Pathfinder Effort. Weather and Forecasting. 40, 1529–1542.
1.
2.
3.

## Slide 5
P90/10 is 90th/10th percentile of skill of all 2000+ HUC8s across the U.S.
Precipitation Forecast Skill
Low
High
P90
P10
Lead Time (days)
Duwamish
Russian
North Fork Feather
Upper Yuba
North Fork
American
Santa Ana
Middle Iowa
Cordeira et al. (2025)
Current “FIRO” watersheds contain skill in the top-10% nationally
Examples from Individual Watersheds (Daily Perspective; Top-5%)

## Slide 6
Factors Influencing Skill: Seasonality
a. GEFS-R 72-h QPF Skill | Top-5% | Cool Season
b. GEFS-R 72-h QPF Skill | Top-5% | Warm Season
Critical Success Index
Cool minus Warm
72-h Aggregate skill higher during cool season as compared to warm season, with some exceptions (using an annually defined top-5% threshold)
For CSI >0.33: 25% of watersheds meet threshold annually; 43% of watersheds meet threshold during cool season

## Slide 7
Factors Influencing Skill: Storm Types
a. GEFS-R 72-h QPF Skill | Top-5% | Atmospheric River
b. GEFS-R 72-h QPF Skill | Top-5% | Non-Atmospheric River
Critical Success Index
72-h Aggregate skill higher associated with AR storm types as compared to non-AR storms (using an annually defined top-5% threshold; ARs defined on QPE days using Gual and Waliser tARget v3 methodology)
For CSI >0.33: 25% of watersheds meet threshold annually; 30% of watersheds meet threshold with ARs.
Cool minus Warm

## Slide 8
Factors Influencing Skill: Storm Types
a. GEFS-R 72-h QPF Skill | Top-5% | Atmospheric River
b. GEFS-R 72-h QPF Skill | Top-5% | Non-Atmospheric River
Critical Success Index
72-h Aggregate skill higher associated with AR storm types as compared to non-AR storms (using an annually defined top-5% threshold; ARs defined on QPE days using Gual and Waliser tARget v3 methodology)
For CSI >0.33: 25% of watersheds meet threshold annually; 30% of watersheds meet threshold with ARs. Change is even larger (25%  58%) for 1-day QPF skill as compared to 3-day QPF skill. (75% of FIRO sites have lead times < 3 days).
Cool minus Warm

## Slide 9: FIRO Screening Process – Stage A Regional Results
All regions have relatively short T+R time scales (1–3 day lead time), most frequent being 1 day
Despite any variations in T+R time, Western watersheds typically exceed CSI criteria
Great Plains has lower CSI across all T+R timelines (despite any aggregation of precipitation)
Region Key

## Slide 10: Critical dimensions of forecast skill methods
Which regional area is used to determine forecast skill?
What is the travel and release time from the reservoir to downstream control points?
T+R = 5 days
Compute the critical success index for the precipitation accumulation matching the T+R
From Prat and Nelson 2014, Hydrology and Earth Systems Science Discussion
Address differences in QPE (observations)

## Slide 11: FIRO Screening Process – Stage A Sensitivity Analysis
T+R = Travel + Release Time
x-axis CSI threshold every 0.01
CSI is CSI at lead time associated with T+R
Basin size, travel and release times, and season all have an impact on the number of sites exceeding a CSI > 0.33
Increasing area of basin means a wider target area (larger number of cells to be averaged, smoother field)
Warm season precipitation (Apr–Sept) has smaller CSI distribution over the CONUS, cool season precipitation (Oct–Mar) has more skill

## Slide 12: What does this mean for the FIRO Screening Process?
Findings | Actions
70% of reservoir catchments areas have a size =< HUC8 size | For reservoir catchments larger than HUC8, skill of HUC6 is used
Choice of QPE dataset did not impact results much (small differences) | Use higher of the two scores
Explore sensitivity on T+R | Reverse engineered what potential flood pool space could be given lead time when CSI>0.33
Differences in cool/warm season skill | Implementing question about seasonal operations in Stage B instrument

## Slide 13
Summary
Applications such as FIRO rely on skillful precipitation and streamflow/inflow forecasts.
We quantified long-term skill to screen watersheds that may have high enough skill to support FIRO.
Skill varies regionally, which is influenced by seasonal differences in storm types.
Application of FIRO in “marginal” skill regions may benefit from further study, especially if operations are seasonal or could benefit from storm-based targeted skill improvement campaigns.

## Slide 14
Applications such as FIRO rely on skillful precipitation and streamflow/inflow forecasts.
We quantified long-term skill to screen watersheds that may have high enough skill to support FIRO.
Skill varies regionally, which is influenced by seasonal differences in storm types.
Application of FIRO in “marginal” skill regions may benefit from further study, especially if operations are seasonal or could benefit from storm-based targeted skill improvement campaigns.
Summary
AR Recon during WY23 improved GFS forecasts by ~3–12%
F. Martin Ralph (UCSD/SIO/CW3E) - PI
Vijay Tallapragada (NWS/NCEP) - Co-PI

## Slide 15
CW3E’s QPF Skill Roadmap
Observations
Modeling
Improve Initial Conditions (e.g., AR Recon)
Research
&
Verification
Improve Parameterization
& Model Configurations
(e.g., West-WRF)
Improve Understanding
of Processes, Storm Types, Skill
(e.g, AR/Precip Science)
Develop Decision Support
Tools & Applications
(e.g., FIRO)
jcordeira@ucsd.edu | cw3e.ucsd.edu