## Slide 1
FIRO Status
Workplan
Complete: 2024
Least bell's vireo, USFWS, Public Domain, https://www.fws.gov/media/least-bells-vireo
asda
Co-Chairs
F. Martin Ralph (Center for Western Weather and Water Extremes at Scripps Institution of Oceanography)
Cary Talbot (US Army Corps of Engineers)
Stuart Vaughan (Tacoma Water)
Members
Joe Forbis (US Army Corps of Engineers)
Sara Marxen (US Army Corps of Engineers)
Stephen King (NOAA, Northwest River Forecast Center)
Mary Strazer (King County Flood Management)
Eric Warner (Muckleshoot Indian Tribe)
Lisa Abernathy (NOAA, National Marine Fisheries Service)
Howard A. Hanson Dam
Top 10 Lessons Learned
2025 and Beyond
Howard A. Hanson Dam Facts
Steering Committee
Collaborating with project partners on network analysis of existing observations, site scouting, and evaluating/planning field data collection and dissemination mechanisms
Extending established meteorological analyses and verification procedures to the Pacific Northwest
Coordinating with Seattle District to locate and leverage existing hydrologic analyses to support the Preliminary Viability Assessment (PVA), and to explore USACE modeling tools
Taking steps to generate hindcasts of ensemble streamflow predictions for the Green River system using NOAA NWS Northwest River Forecast Center (NWRFC) hydrologic models this summer
Developing a simulation plan for processing and evaluating the streamflow hindcasts across a range of possible operational alternatives for reservoir management at HAHD
Exploring collaborative and streamlined project management practices and tools to foster transparency and efficiency in our work
Planning for the next Steering Committee meeting in late September (in Tacoma)
Howard A. Hanson Dam (HAHD) is an earthen embankment dam on the Green River in King County, Washington, completed in 1961 by the U.S. Army Corps of Engineers
The dam’s primary purpose is flood risk management for the heavily populated Seattle–Tacoma metropolitan area
The dam creates no permanent reservoir, but has a temporary flood storage capacity of approximately 106,000 acre-feet
The Green River watershed upstream of the dam covers ~220 square miles
HAHD plays a vital role in protecting critical infrastructure, residential areas, and regional economic assets in South King County
FIRO has been identified as a promising approach to enhance the dam’s flood management and water supply coordination
FIRO
Howard A. Hanson
Preliminary Viability Assessment
In-Progress,
Final: Dec 2026
Final Viability Assessment
Final: 2028
Steve Ringman, The Seattle Times
Vancouver Aquarium/NOAA/Jamie Lusch
Turns out water has a lot of “flavors”, and water accounting can pose complex modeling challenges
Can't overstate the importance of establishing and nurturing strong relationships and communication
Scheduling in-person meetings across inter-agency groups is no small feat
Our coordinators and consultants are keystone species!
Standardized approaches to managing tasks and meetings are key as we grow and share responsibilities
Local partner input and regional insight play a critical role during the network analysis, as they guide decisions about site selection and deployment strategy
Expect curve balls (from any direction and/or level)
Time flies, and so it’s best to keep things warm
Critical to identify, respect, and leverage the expertise and resources of each group/agency
Recognize (and appreciate) that we're all in this for the right reasons, even if reasons differ and could be at odds

## Slide 2
Draft Preliminary Viability Assessment will be finished January 2026 and finalized October 2026
Next steering committee meeting planned for October 8th, 2025
Work teams are making progress for the PVA to begin writing in September 2025
Groundwater recharge operations models developed for four locations within the San Bernardino Basin area
Water resources engineering team is simulating baseline operations and 16 FIRO alternatives (4 FIRO strategies x 4 FIRO spaces) in the PVA
Environmental team has identified quantitative metrics to assess FIRO alternatives
Observation team is working with local sponsors to identify suitable streamflow gage location
San Bernardino Valley and CW3E are brainstorming how to model water quality to include in the FVA
Considering deviation request when PVA is near completion
Final Viability Assessment will be drafted by late 2027 and finalized by late 2028
Seven Oaks Dam is a roller-compacted concrete gravity dam on the Santa Ana River.
The resulting impounded water is called the Seven Oaks Reservoir.
Planning for the dam began in the 1960s in response to severe flood risks in the Santa Ana River watershed.
The dam’s construction was completed in 2000.
The Seven Oaks dam’s primary purpose is flood risk management. Other downstream interests include groundwater recharge and environmental flow considerations.
The dam can store up to 145,600 acre-feet of water during flood events.
Unlike many dams, Seven Oaks does not maintain a permanent reservoir and remains dry outside of storm season.
The dam is part of the Santa Ana River Mainstem Project and complements the downstream Prado Dam for regional flood control.
Co-Chairs
Heather Dyer (San Bernardino Valley Municipal Water District)
F. Martin Ralph (Center for Western Weather and Water Extremes at Scripps Institution of Oceanography)
Cary Talbot (US Army Corps of Engineers, Engineer Research and Development Center)
Members
Michael Anderson (California Department of Water Resources)
Rebecca Christensen (U.S. Fish & Wildlife Service)
Michael Fam (San Bernardino County Public Works)
Joe Forbis (US Army Corps of Engineers)
Mallory O’Conor (Western Municipal Water District)
Lisa Haney (Orange County Water District)
Jayme Laber (NOAA Weather Services) Betsy Miller (San Bernardino Valley Water Conservation District)
Jennifer Ramos Ortiz (US Army Corps of Engineers) James Tyler (Orange County Public Works)
Greg Woodside (San Bernardino Valley Municipal Water District)
Think about FIRO from the perspective of the dam owner – what additional risk they would take on and would they have the resources to implement FIRO.
Precipitation forecast skill is strongly influenced by the location and timing of landfalling ARs and associated variability in the freezing level that subsequently impacts the timing and overall amount of runoff.
It may be difficult to stress test the system with inflows over the hindcast period of record. Synthetically generated forecasts for larger events in the historic record are a useful tool to test the system’s limits.
No one knows a watershed like the people that work there every day; partner input is critical to understanding where additional observations will have the most impact.
Water quality changes in the reservoir may play an important role in operational considerations.
It's important to consider the management of upper and lower portions of a watershed and coordinate as needed.
Confirm observation data is readily available and conduct skill assessment of hindcasts at the beginning of PVA to avoid delays later in the PVA.
Better documentation about which components of a FIRO strategy are generalizable versus project specific could improve knowledge transfer.
Trash racks don’t play fair. Existing infrastructure or operational constraints may limit FIRO benefits. We need to think outside the box but inside the bubble to address constraints within the current operational paradigm.
Sometimes at least 15 schematics of the system are needed to understand all the ways water can move in the system.
FIRO Status
Workplan
Complete: 2024
FIRO
Seven Oaks
Seven Oaks Dam
Top 10 Lessons Learned
2025 and Beyond
Seven Oaks Dam Facts
Steering Committee
Steve Schumaker via Wikimedia Commons released under CC BY-SA 1.0.
Preliminary Viability Assessment
In-Progress,
Final: Oct 2026
Final Viability Assessment
Final: 2028

## Slide 3
Least bell's vireo, USFWS, Public Domain, https://www.fws.gov/media/least-bells-vireo
asda
Co-Chairs
F. Martin Ralph (Center for Western Weather and Water Extremes at Scripps Institution of Oceanography)
John James (Yuba Water)
Molly White (California Department of Water Resources)
Members
Michael Anderson (California Department of Water Resources)
Cary Talbot (US Army Corps of Engineers)
Joe Forbis (US Army Corps of Engineers)
Jenny Fromm (US Army Corps of Engineers)
Brett Whitin (CA/NV River Forecast Center)
Yuba-Feather Watershed
Top 10 Lessons Learned
2025 and Beyond
Steering Committee
Quarterly Steering Committee meetings are continuing post-FVA as the project turns to implementation.
WCM update NEPA scoping is planned for 2025 with targeted NEPA completion in 2026 and WCM updates completed in 2027.
WCM update is being done in a way that accounts for the new ARC Spillway to assist with adoption after the construction is complete.
ARC spillway filed a major permit application in June and July 2025 and now is awaiting Board approval to proceed with construction.
ARC Spillway construction start is projected in 2027/28 and completion is 3-4 years after.
New Research efforts are focused on a partnership with CNRFC to improve forecasts inputs into HEFS and 10-day deterministic streamflow forecasts for FIRO in the Yuba-Feather. These efforts will also utilize the robust observation networks deployed by F-CO, FIRO, and other programs.
DWR and Yuba Water have incorporated AR forecasts into briefings and reports.
The F-CO Program is including AR forecasts in this year's functional exercise, and once WCM updates are finalized it will incorporate the new operations into the Yuba-Feather decision support system.
FIRO Status
New Bullards Bar (NBB) Dam is on the North Yuba River, was completed in 1970, and has a total storage capacity of approximately 970,000 acre-ft.
Primary purposes of NBB include flood control, water supply, hydroelectric power, and recreation.
Yuba Water Agency is building a new Atmospheric River Control (ARC) Spillway designed with gates 31.5 ft lower than the current spillway.
Oroville Dam (ORO), on the Feather River, was completed in 1968 creating Lake Oroville with a storage capacity of about 3.4 million acre-feet.
Built and operated by the California Department of Water Resources (DWR), ORO is the tallest dam in the U.S., at 770 feet
ORO part of the State Water Project, supplying water for a variety of sectors.
The Forecasted-Coordinated Operations Program (F-CO) coordinates between NBB and ORO to mitigate impacts at the confluence of the Yuba and Feather rivers near Marysville and Yuba City.
FIRO
Yuba-Feather
Workplan
PVA
FVA
Complete: 2021
Complete: 2022
Complete: 2025
cw3e.ucsd.edu/firo_yuba_feather
New Bullards Bar & Oroville Facts
Dam owners/operators’ robust public outreach and communication, coupled with local school engagement, helped build public awareness and support.
Forecast Coordinated Operations Program provided a strong foundation of partnerships for FIRO and WCM Update engagement.
Using HEC Res-SIM for viability assessments and ensuring capability with CWMS is essential for FIRO integration into Corps operations.
Lack of a period of record analysis in the viability assessment limits the ability to make conclusive statements about water availability benefits.
Primary FIRO metrics associated with water availability are easier to achieve than a primary metric of flood mitigation when the dams are designed and operated to mitigate large floods.
Accumulated 72-hour inflow volumes are more skillful than originally anticipated; verification studies showed skillful forecasts going out to 7-9 days.
Consulting with NEPA experts early in the process resulted in a phased approach rather than two WCM updates for the proposed ARC spillway at New Bullards Bar Dam.
FIRO operations, coupled with a proposed ARC spillway, were able to achieve nearly the same flood control space-over 260.000 ac-ft- as an authorized but unconstructed reservoir.
Launching weather balloons from a warehouse during an AR at 3 AM would make a great intro to horror movie.
A Steering Committee can spend a really long time talking about the shades of green in a table.

## Slide 4
Even the smallest things can have the biggest effect on cost and schedule—Habitat support for Least Bell’s Vireo 🦜
Early and frequent engagement with USACE at the District and Division levels is critical 📞
FIRO enabled approval of the 5-year minor deviation (508’) at Prado Dam 💧
Success of FIRO at Prado Dam stems not just from additional amounts of recharge but also from broader investments by the Corps into the FIRO initiative 🏗️
Incorporating the EFO control strategy into HEC-ResSim is not easy 💻 🧩
Improving meteorological forecasts for the wettest 5% days of the water year has the greatest potential to benefit 🌧️
Effectively communicate ensemble/probabilistic information available in CW3E forecast products to support the reservoir operator’s decision-making process 📊
Digital twin is an innovative technology that supports informed water operations by integrating environmental health into decision-making 📡
Please pay attention to proper identification of the NEPA and NHPA scope of analysis and Area of Potential Effects 📚
Important to continue the Steering Committee meetings after viability assessment is complete 🪑
FIRO
Prado Dam
asda
Co-Chairs
Lisa Haney (Orange County Water District)
Hayley Lovan (U.S. Army Corps of Engineers, Los Angeles District)
Members
F. Martin Ralph (Center for Western Weather and Water Extremes at Scripps Institution of Oceanography)
Michael Anderson (California Department of Water Resources)
Cary Talbot (US Army Corps of Engineers)
James Tyler (Orange County Public Works)
Tim Fairbank (US Army Corps of Engineers)
Joe Forbis (US Army Corps of Engineers)
Greg Woodside (San Bernardino Valley Municipal Water District)
James Tyler (Orange County Public Works)
John Sweeten (US Army Corps of Engineers) Cuong Ly (US Army Corps of Engineers) Rebecca Christensen (US Fish and Wildlife Service) Peter Fickenscher (National Oceanic and Atmospheric Administration)
Prado Dam
Top 10 Lessons Learned
2025 and Beyond
Prado Dam Facts
Least bell's vireo, USFWS, Public Domain, https://www.fws.gov/media/least-bells-vireo
Steering Committee
FIRO Status
Workplan
PVA
FVA
Complete: 2019
Complete: 2021
Complete: 2023
Figure 2. Current water conservation pool program at Prado Dam. Source: OCWD
Post-FVA Prado Dam Steering Committee (SC) held its Kick-Off meeting in May 2025. Co-chairs are Lisa Haney (OCWD) and Hayley Lovan (USACE).
Minor 5-year deviation approved (increase from 505’ to 508’). Adjustment will allow for the capture of an additional two billion gallons of stormwater, which is enough water to supply 48,000 people and save $6 million in imported water costs.
Technical workshops and coordination strategies planned between USACE LA District, OCWD, and CW3E, for FIRO implementation at Prado Dam.
Forecast products and decision-support tools tailored to the Santa Ana River watershed to support real-time operations and maximize recharge with environmental considerations.
Developing an AI Digital Twin to assess the impacts of higher pool on habitat of endangered Least Bell's Vireo behind the dam for monitoring FIRO’s environmental impacts/benefits.
On schedule for WCM update #1 (2027) and #2 for FIRO operations (2029).
Continue to build on partnerships started during the OCWD/Xylem/CW3E/USGS/USACE LA District collaborative and successful effort to improve gage measurements at Prado Dam.
Prado Dam was constructed by the U.S. Army Corps of Engineers (USACE) in 1941.
Prado Dam stretches across the Santa Ana River, which is more than 90 miles long and is the longest river entirely within Southern California. Its effective contributing drainage is ~2,450 sq miles, 92 percent of which is controlled by Prado Dam.
Santa Ana River tributaries originate in the San Bernardino Mountains and flow southwest through San Bernardino, Riverside, and Orange Counties before emptying into the Pacific Ocean.
Orange County Water District (OCWD) has been capturing and recharging stormwater from the Santa Ana River since 1936.
USACE, which also operates the dam, has been collaborating with OCWD to temporarily impound water and release it from the dam to facilitate recharge of the OC groundwater basin, which is a key source of water to over 2.5 million people.
Prado Basin houses the single largest forested wetland in coastal Southern California, supporting an abundance and diversity of wildlife, including the Least Bell’s Vireo that depend on the critical riparian habitat of the basin.
Least Bell’s Vireo (Vireo bellii pusillus)
Photograph by Alexandra Houston,
U.S. Geological Survey

## Slide 5
Least bell's vireo, USFWS, Public Domain, https://www.fws.gov/media/least-bells-vireo
For USACE-managed reservoirs, viability assessments are collaborative efforts that are difference from WCM updates but can inform them.
Local partner agencies have contributed significantly to the success of FIRO via staff resources and/or financial support.
Collaboration between a diverse group of stakeholders, and relevant performance metrics, is essential for a successful FIRO program.
Skillful forecasts of atmospheric river precipitation and long dry periods, combined with FIRO strategies, have routinely yielded additional water, including 30,000 acre-feet in 2025.
Ensemble precipitation and hydrologic forecasts are important to more fully characterize uncertainty.
Deviations to the Water Control Diagram support research and operations partnership (RAOP)
Pre-releases in advance of storms can greatly improve flood risk management, but must be coordinated with other agencies that have conservation storage rights.
Development of FIRO alternatives should focus on size and geometry of the FIRO zone, rather than a specific model type or forecast.
Connections to landowners via local agencies are invaluable for quickly siting, deploying, and operating robust and dense observational networks
Russian River tributaries are an excellent way to cool off and refresh after long hydrometeorological station install days.
asda
Co-Chairs
Don Seymour (Sonoma Water)
F. Martin Ralph (Center for Western Weather and Water Extremes at Scripps Institution of Oceanography)
Nick Malasavage (US Army Corps of Engineers)
Members
Michael Anderson (California Department of Water Resources)
Chris Frans (US Bureau of Reclamation)
Joe Forbis (US Army Corps of Engineers)
Joshua Fuller (National Marine Fisheries Service)
Cary Talbot (US Army Corps of Engineers)
Brett Whitin (NOAA’s NWS California Nevada River Forecast Center)
Patrick Sing (US Army Corps of Engineers)
Russian River Watershed
Top 10 Lessons Learned
2025 and Beyond
Lake Mendocino Facts
Steering Committee
WY 2025 operations in accordance with rule curve deviations at Lakes Mendocino and Sonoma yielded approximately 30,000 AF of additional water in storage representing another successful year of water management implementing FIRO.
Lake Sonoma is being considered as a pilot project to test enhancement to CWMS made by HEC. SPN and SW support its inclusion.
There is an opportunity to leverage AQPI radars by increasing radiosondes at Bodega Bay to address QPF underestimates for the coastal mountains.
Lake Mendocino WCM - BiOp has been issued, and the WCM update should be finalized in October, following the public comment period ending in late July.
An educational display (small poster size) is being planned for a public-access trail along the crest of the Coyote Valley Dam (Lake Mendocino) embankment. It will include basic information about FIRO and key outcomes for water storage and flood risk mitigation, among other interesting factoids.
FIRO Status
Coyote Valley Dam, completed in 1959, is an earthfill dam on the East Fork Russian River, forming Lake Mendocino in Mendocino County, CA
It was built by the U.S. Army Corps of Engineers and is co-managed with Sonoma Water
The watershed upstream of the dam covers about 105 square miles
The dam serves flood risk reduction, water supply, fisheries protection, and recreation, but does not generate hydropower
Lake Mendocino supplies water to parts of Sonoma and Mendocino counties, including flows for endangered fish species
In the past, inflexible flood operation rules led to early-season water releases that sometimes resulted in supply shortfalls later
FIRO was piloted here starting in 2014, making it the first operational FIRO project in the U.S.
The FIRO Russian River project benefits from a hybrid network with diverse observation deployed over several decades, with over 20 distinct sites installed as part of FIRO projects.
FIRO
Russian River
Workplan
PVA
FVA
Complete: 2015
Complete: 2017
Complete: 2020
Photo of Lake Mendocino Steering Committee (2018) by Cary Talbot