## Slide 1: Don Seymour, P.E. Deputy Director of Engineering
Forecast Informed Reservoir Operations and Environmental Considerations in the Russian River
August 4, 2025

## Slide 2: Topics
Russian River Watershed
Russian River FIRO Timeline
FIRO in the Russian River
Status of Russian River FIRO
Russian River Biological Opinion
Environmental Considerations
Notes: The Corps Russian River Project won out.
In order to become the local sponsor of the Corps project to use the water in Lake Mendocino to meet municipal needs, the Sonoma County Water Agency was established in 1949 through a special act of the Legislature.
The first component of the Russian River Project, Lake Mendocino, was completed in January 1959 and was full a month later, thanks to heavy rains.

## Slide 3: FIRO Intersection with Environmental Considerations
Key Take Aways
FIRO procedures implemented through planned deviations at both Lake Mendocino and Lake Sonoma have enhanced Sonoma Water’s and USACE ability to meet requirements and objectives of the Russian River Biological Opinion. This includes:
Preserving the cold-water pool at Lake Mendocino
Reducing the magnitude and duration of flood control releases by making prereleases using FIRO decisions support tools.
Sonoma Water’s commitment to make adaptive releases from Lake Mendocino and providing 2,500 acre-feet of block water in Lake Sonoma to enhance migration of salmonids into and out of the Russian River

## Slide 4: Russian River Watershed Dual Purpose Facilities Flood protection (USACE) Water supply (Sonoma Water) Operations dictated by storage levels relative to FCM guide curve Lake Mendocino Flood control pool: 48,100 AF Water supply pool: 68,400 AF (11/1 –3/1) Lake Sonoma Flood control pool:136,000 AF Water supply pool: 245,000 AF
Lake Mendocino
Lake Sonoma

## Slide 5: Russian River FIRO Timeline
2014 – Lake Mendocino FIRO Steering Committee formed
2017 – Lake Mendocino Preliminary Viability Assessment completed
2018 – Minor Deviation to the Lake Mendocino Flood Control Manual approved
2019 – Major Deviation to the Lake Mendocino Flood Control Manual approved
2020 – Lake Mendocino Final Viability Assessment completed
2020 – Major Deviation to the Lake Mendocino Flood Control Manual approved
2021 – Multiyear (2021 – 2026) Major Deviation to the Lake Mendocino Flood Control Manual approved
2022 – Minor Deviation to the Lake Sonoma Flood Control Manual approved
2023 – Minor Deviation to the Lake Sonoma Flood Control Manual approved
2024 – Multi-year (2024 – 2026) Minor Deviation to the Lake Sonoma Flood Control Manual approved

## Slide 6: Lake Mendocino Storage & Encroachment Curve

## Slide 7: Lake Sonoma Storage & Encroachment Curve

## Slide 8: Status Of FIRO In The Russian River
Lake Mendocino
July 17, 2025 – USACE released the draft Environmental Assessment for the Lake Mendocino Water Control Manual update
30-day comment period
Anticipate USACE finalizing the updated manual by late October 2025
Lake Sonoma
The Russian River FIRO Steering Committee has started assessment of FIRO
Hydro meteorological network has been installed
FIRO will be evaluated in detail for the existing outlet configuration and, if viable will lead to a WCM update to include FIRO procedures
FIRO will also be evaluated at a conceptual level for a secondary outlet to assess leveraging benefits for water supply and flood risk management

## Slide 9: Russian River Biological Opinion
2008 Russian River Biological Opinion
Jeopardy opinion regarding water supply and flood control operations performed by Sonoma Water and USACE
Fifteen-year term, expired in September 2023
Activities likely affect Central California Coastal Steelhead, Central California Coastal Coho and California Coastal Chinook
Activities Also Likely Affect the Habitat of These Species.
2025 Russian River Biological Opinion
Non-jeopardy opinion as a result of Reasonable and Prudent Measures implemented by USACE and Sonoma Water during the term of the 2008 Biological Opinion
10-year Term and covers operations and maintenance activities for USACE and Sonoma Water flood control and water supply activiies
Evaluated FIRO procedures at Lake Mendocino and Lake Sonoma
Includes adaptive reservoir release strategies to improve fish migration

## Slide 10: Environmental Considerations for FIRO in the Russian River
Lake Mendocino Final Viability Assessment
All FIRO alternatives outperformed baseline in improving end of the year water storage, extending the cold-water pool later into the fall/early winter
All FIRO alternatives outperformed baseline in reducing the duration and magnitude of flood control releases that impact spawning of Chinook salmon and their habitat

## Slide 11: Environmental Considerations for FIRO in the Russian River
2025 Russian River Biological Opinion
Reduced magnitude and duration of flood control releases
Increased storage preserves cold water pools at both reservoirs
Adaptively manage Coyote Dam releases
2,500 acre-feet of block water from Lake Sonoma to be used for enhancing seasonal fish migration through pulse flows per NMFS direction
NMFS supports implementation of FIRO procedures

## Slide 12
Don Seymour, P.E.
Deputy Director of Engineering
Donald.Seymour@scwa.ca.gov