## Slide 1: Environmental Considerations for FIRO at Seven Oaks Dam
FIRO August 2025 Workshop
Greg Woodside & Chris Jones
gregw@sbvmwd.com chrisj@sbvmwd.com

## Slide 2: Environmental Considerations for FIRO at Seven Oaks Dam - Summary
Provided by: Greg Woodside & Chris Jones
Key Topics: | Key Takeaways:
Multiple species and habitats of interest: fish, mammals, birds, herps, and plants Metrics are identified in three focal areas Exploring options to release water from the dam in a manner that will enhance habitat Water quality considerations are important | Consideration of multiple special status species and habitats makes for complex analysis. Options to benefit one type of habitat may harm a different habitat. Environmental metrics are generally clustered around potential impacts of changes in dam operations and associated changes in frequency, duration, and incidence of changes to pool elevations, downstream flow, and water quality.

## Slide 3: Regional Location Map

## Slide 4: Special Status Species
Special-status species occurrence throughout the calendar year and associated level of concern. High concern indicates species’ breeding season and potential presence. Moderate concern indicates non-breeding season and potential presence.

## Slide 5: Environmental Team Structure
Participating Organizations
  USFWS
  USACE
  USDA Forest Service
  CDFW
  County of Orange
  OCWD
  SBVWCD
  CW3E
  San Bernardino County
  Center for Biological Diversity
  Endangered Habitats League
Team Leads
  Chris Jones (SBVMWD)
  Rebecca Christensen (USFWS)

## Slide 6: Example Metrics: Upstream Focal Area
US-1: Number of days of inundation above the following water surface elevations: top of intermediate pool (2265'), trash rack pool (2299'), 2,350', 2,400ft.
US-2: Incidence of adverse water quality changes during temporary storage in the pool (e.g., HABs, turbidity, temperature, DO, pH, ).

## Slide 7: Example Metrics: Alluvial Fan Focal Area
AF-1a: Number of days flow in the river exceeds 100, 200, 300, 400, 500, 1000, 1500, 2000, 2500 cfs or greater in river channel (after diversions accounted for)
AF-2a: Number of days flow is intentionally discharged out of enhanced recharge facility to maintain RAFSS habitat.

## Slide 8: Metrics: Perennial Stream Focal Area
PS-1a: Number of days flow in the river exceeds 100, 200, 300, 400, 500, 1000, 1500, 2000, 2500 cfs or greater in river channel at the upstream end of the perennial stream focal area when releases are being made from Seven Oaks Dam per water year.
PS-2: Turbidity, pH, temperature and dissolved oxygen levels for water released from the dam that would remain in the river after diversions and recharge potential is accounted for

## Slide 9: Example Metrics: Perennial Stream Focal Area
PS-3a: Number of days a release reaches the perennial stream that is driven by maintenance needs, need to evacuate pool to accommodate a pending storm, or when water quality is unsuitable for recharge purposes.

## Slide 10: Current Monitoring, Research, and Studies
Water Quality Monitoring
  Storm and non-storm monitoring
  Base lapse photography of pool (monitor for algae bloom)
Repeat Photography: tracking landscape change over time
  Aerial Imagery and LiDAR
  Wildlife monitoring
  Photo stations

## Slide 11: Upcoming Monitoring, Research and Studies
Post-Line Fire Workshop and Studies
  Water Quality/Quantity
  Sediment Transport
  Mass Loading
  Dry Ravel Mapping
  Habitat Recovery
Water Supply
  Natural Reservoirs
    Snowpack
    Meadows
Photo credit: 1: Redspork02, Wikipedia.com accessed 5-30-2025

## Slide 12
Includes WQ data and WQ model; describes 3 major modes of interaction
Describes proposed changes to operation of Debris Pool (which were not implemented)

## Slide 13
Modes of Interaction
Third Mode: re-suspension of sediment downstream of dam
‘The 2010 and 2011 release tests further showed that the extreme high turbidity seen in the immediate downstream reaches below SOD is not generated within the pool, but is due largely to re-suspension or scour of bed and bank material in the SAR channel. From the July 2010 and February 2011 testing it is apparent that high flow can mobilize finer materials in the stream bed and bank with a pronounced “first flush” effect.’

## Slide 14
‘Overall, the data from 2010 and 2011 suggest strongly that the extended duration of turbidity in releases from SOD during (or following) typical winter floods is a largely unavoidable consequence of flood retention with an extended release, rather than the result of in-pool generation of turbidity creating materials (i.e., by generation of algal blooms or release of dissolved substances from bottom sediments).’

## Slide 15: Items to Consider in Scoping Water Quality Evaluation
Review if data collected since 2011 ERDC report are consistent with ERDC report findings
To what extent can releases of water stored at SOD negatively impact downstream water quality?
Would modeling water quality changes during storage at SOD provide beneficial information?
What additional data may be needed to support modeling and decision making?
To what extent can water quality in the SOD reservoir area be managed/controlled?
  Modification to eliminate/reduce dead pool (if there is a dead pool)
  Other options

## Slide 17
June 10, 2025
March 25, 2025