## Slide 1: Forecasting within CWMS/HEC-RTS
Matt Fleming, P.E.
Hydrologic Engineering Center
Annual FIRO Training and Workshop

## Slide 2: Forecasting within CWMS/HEC-RTS
Key Topics: | Key Takeaways:
Overview of the Corps Water Management System (CWMS) / Real Time Simulation (HEC-RTS) Software Software capabilities are contained within HEC-RTS to assist with FIRO The Ensemble Forecast Processor is a newer addition to HEC-RTS Future development and improvements have been identified; feedback welcome | CWMS is the USACE Enterprise toolkit for data acquisition, forecasting, reservoir operations, consequence analysis, and data dissemination HEC-RTS includes components to simulate uncertainty in the meteorologic and hydrologic forecast, which are linked to a reservoir simulation tool The Ensemble Forecast Processor (EFP) is a tool for computing ensemble metrics and identifying ensemble members for using in reservoir operations; an example application is available

## Slide 3: Overview
CWMS Overview
Primary Forecasting Options within HEC-RTS
HEC-RTS Ensemble Compute
HEC-RTS Ensemble Forecast Processor
Example Application

## Slide 4: Corps Water management System (CWMS) Overview
Notes: CWMS Overview

## Slide 5: Corps Water Management System (CWMS)
CWMS is Automated Information System (AIS) to collect, process, and store real-time data
The Real Time Simulation (HEC-RTS) software is a suite of modeling tools to run real-time forecast simulations and help achieve a wide range of reservoir authorized purposes
Designed and evolving to meet USACE initiatives, the WM mission, and other legislative requirements
HEC-RTS version 3.5 will be available from the HEC website in September 2025: https://www.hec.usace.army.mil/software/hec-rts/downloads.aspx

## Slide 6: CWMS CAVI/HEC-RTS
Control and Visualization Interface (CAVI)
  Integrates real-time data acquisition, data visualization and modeling tools
Instructions
Data

## Slide 7: HEC-RTS Modeling Tools
Hydrology
Reservoir Operations
Hydraulics
Consequences
Meteorology

## Slide 8: Meteorological Scenarios: HEC-MetVue
Processes and Combines Observed and Forecast Meteorological Datasets
  Precipitation, Temperature, and more
Allows for:
  Observed Dataset Corrections
  Forecast Dataset Adjustments for Additional “What-If” Scenarios

## Slide 9: Hydrologic Modeling: HEC-HMS
Compute runoff and uncontrolled flows given input meteorological data
Predict inflows to reservoirs, and local-flows downstream of reservoirs
Spatially distributed continuous simulation options
Model output used as input to reservoir operations and hydraulics models

## Slide 10: Reservoir Operations: HEC-ResSim
Given stream flows and water control rules, simulate reservoir operations
Override operations to test operating plan scenarios
Model output used as input to hydraulics and consequences models

## Slide 11: River Hydraulics: HEC-RAS
Given flow hydrographs, compute water surface profiles
Predict resultant water surface elevations and inundation areas for events
Produce inundation maps
Model output used as input to consequences models
Notes: 11

## Slide 12: Consequences: HEC-FIA
HEC-FIA (Flood Impact Analysis) identifies the consequences from a flood event
Given river stages and damage data, computes damages to structures and estimates life loss
Computes project benefits
Response tables provide a list and of actions to take during an event, based on forecasted stages

## Slide 13: CWMS National Implementation Plan
  $124 million 15-year program (2012-2026)
  Build out of CWMS basin models in all 7 continental divisions and Alaska
  Around 200 USACE personnel per year worked on CWMS implementation including engineers, economist, and GIS specialists
  Models are used on other studies and are updated/improved
Notes: CWMS Overview

## Slide 14: 100% CWMS IMPLEMENTATION
An office with water management responsibility MUST have Corps Water Management System (CWMS) models developed and be fully capable to run the full suite of models (complete with meteorological and reservoir scenarios) to completion with consequences and inundation mapping being produced.
The office MUST regularly exercise the models to ensure they are sufficient in their operation/use/application and have an exercised Continuity of Operations Plan (COOP) in-place.
CWMS models MUST replace legacy systems since CWMS is the USACE standard across the enterprise.
It is expected that CWMS models will be used for daily operational planning in determining appropriate operational actions for reservoir operation.
Notes: CWMS Overview

## Slide 15: Primary Forecasting Options within HEC-RTS
Notes: CWMS Overview

## Slide 16: CWMS / HEC-RTS Forecasting
HEC-RTS can be configured to create multiple forecasts, each using different forecast products and the same or different hydrologic and reservoir simulation configurations / parameterizations.
For USACE staff, precipitation forecasts are downloaded from Cumulus. External forecasters can download and process external meteorologic forecasts and store the information in a local DSS file.

## Slide 17: CUMULUS – Provides meteorologic Forecasts to USACE
CWMS supports Cumulus directly:
CorpsNet/VPN access with CAC authentication
https://cumulus.corps.cloud/
HRRR – 1hr
NBM – 1hr
NDFD – 6hr
WPC – 6hr
NAEFS – 6hr
Notes: NDFD (National Digital Forecast Database) precipitation grids refer to the digital, gridded forecasts of precipitation produced by the National Weather Service.
WPC precipitation grids refer to the gridded quantitative precipitation forecasts (QPFs) produced by the NOAA/NWS Weather Prediction Center (WPC).
The North American Ensemble Forecast System (NAEFS) is a joint project between the Meteorological Service of Canada (MSC) and the U.S. National Weather Service (NWS) that provides precipitation grids and other weather guidance across North America.

## Slide 18: HEC-RTS Ensemble Compute
Notes: CWMS Overview

## Slide 19
Russian River – Guerneville
California Nevada RFC
March Ensemble Forecast

## Slide 20: CAVI Ensemble Compute
What does it do?
  Each trace used sequentially in an isolated pass through the Program Order
  Each trace generates a separate watershed “run” folder in the forecast
  Results in separate forecast.dss files, then rolled into a master forecast.dss at end.
  Current Limitations
  Ensemble input data only from HEC-DSS, not CWMS Database
  Gridded ensembles not yet supported

## Slide 21: HEC-RTS Ensemble Forecast Processor
Notes: CWMS Overview

## Slide 22: Ensemble Forecast Processor (EFP)
What does it do?
  New plugin first available in CWMS 3.4
  Based on HEC-WAT FIRO Forecast Processor
  Part of the HEC-RTS Program Order
  Allows user to specify locations within the watershed to calculate statistical metrics from ensemble time series
    Metrics can be used as input to other applications within the CWMS forecast
  Identifies ensemble members closest to metrics too, which can be used as boundary conditions for model simulations
3-day volume

## Slide 23: Ensemble Forecast Processor
  Scalar Metrics:
  Can be used to influence rules in HEC-ResSim alternatives
  User defined durations and percentiles
  Based on Prado FIRO case study approach
  Scalar values saved to the forecast.dss file

## Slide 24: Ensemble Forecast Processor
  Time Series:
  Allow for reduced number of ensemble members to be used for input to other models
  For a chosen metric(s), returns the specific ensemble member that has the closest volume
  Merges observed time series with the returned ensemble member; time series saved to the forecast.dss file

## Slide 25: Ensemble Forecast Processor (EFP)

## Slide 26: Summarized ensemble forecast
Raw
HEFS Data
Extract
Ensemble Forecast
Processor (EFP)
HEC-RAS + HEC-FIA
DSS
Ensemble DSS
Ensemble DSS
Regulated Flows
Ensemble CSV
Regulated Flows
Metric Data + Uncontrolled Flows
Metric Data
HEC-MetVue
+
HEC-HMS
HEC-ResSim
Gridded DSS
Uncontrolled Flows

## Slide 27: Regulated ensemble forecast
Raw
HEFS Data
Extract
Ensemble
HEC-ResSim
HEC-RAS + HEC-FIA
DSS
Ensemble DSS
Ensemble DSS + Uncontrolled Flows
Ensemble Summary
Ensemble CSV
Ensemble Summary
Regulated Ensemble DSS
HEC-MetVue
+
HEC-HMS
Ensemble Forecast
Processor (EFP)
Gridded DSS
Uncontrolled Flows
Regulated Ensemble DSS

## Slide 28: Example Application
Notes: CWMS Overview

## Slide 29: EFP Example Application
https://www.hec.usace.army.mil/confluence/cwmsdocs/ctg/general-hec-rts/running-the-ensemble-forecasting-processor-in-cavi

## Slide 30: EFP Example Application

## Slide 31: EFP Example Application
Lookback time-series = Observed Flow
Forcaset time-series = Ensemble Dataset
Metrics will be computed for the 3-day volume and the ensemble members closest to the 0.1, 0.5, and 0.9 percentile 3-day volumes will be extracted

## Slide 32: EFP Example Application
The model linking framework provides options for swapping out different ensemble members
The figure shows the HEC-ResSim alternative being linked to the ensemble member that was closest to the 0.5 percentile 3-day volume

## Slide 33: EFP Example Application
NBM + HEC-HMS Forecast
RFC Ensemble Member Forecast
Ensemble member closest to 50th percentile 3-day volume
Ensemble member closest to 10th percentile 3-day volume
Ensemble member closest to 90th percentile 3-day volume

## Slide 34: Forecasting Improvements
Example applications showing how to use HEC-RTS for an ensemble type analysis; including long range forecasts
Incremental improvements to the Ensemble Forecast Processor
  For larger watersheds (key off one location to choose ensemble members)
Forecast skill assessment for hydrologic forecasts (flow and precipitation)
  Identify better performing meteorologic forecasts regionally
Add tooling to combine multiple meteorologic datasets
Improve disaggregation of 6 hour forecast volumes to 1-hour intervals
Build out options to ingest, process, and apply gridded meteorologic ensembles within HEC-RTS (make use of uncertainty analysis options in models)
Add a dashboard to cumulus showing basin average precipitation totals for various forecast products
Improvements in reservoir operations modeling with ensembles, specifically incorporating probabilistic information into the downstream control operation
Better computational methods to deal with system operations

## Slide 35: Questions additional Documentation
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams