## Slide 1: Advances in Machine Learning for Weather Forecasting
Agniv Sengupta, Ph.D.
CW3E Machine Learning Team Lead
12th Annual FIRO Training and Workshop
August 6, 2025

## Slide 2
# 2
ADVANCING FIRO WITH ML ADVANCES IN WEATHER FORECASTING
Key Topics
Key Takeaways
Review current state-of-the-science in AI & ML powered weather forecasting
Postprocessing forecasts with Deep Learning
(a) IVT associated with ARs
(b) Freezing level forecasts
(c) Quantitative precipitation forecasts
AI data-driven weather forecasting
(a) Emergence of AI weather models
(b) AI large ensembles for prediction of extremes
(c) AI-based climate attribution tools
(d) Regional high-res AI weather modeling
To date, weather forecasts informing operations for FIRO has primarily relied on physics-based models.
Significant improvements are being achieved with innovative deep learning algorithms for the prediction of extreme events (e.g., top 1% events), especially at the watershed scale.
Recently developed AI data-driven weather models are significantly transforming the weather prediction enterprise, including the generation of very large ensembles with significantly lesser real-time computational resources.
In the coming years, emerging technologies that integrate dynamical modeling with AI and ML offer promising opportunities to enhance FIRO outcomes.

## Slide 3
Machine learning approaches
Postprocessing
  Long-training
  Short training
Data driven
  Traditional statistical models
  AI data-driven models
Areas of research
Weather (0-10 days)
Subseasonal (2-6 weeks)
Seasonal (1-6 months)
Hydrology
ARTIFICIAL INTELLIGENCE vs MACHINE LEARNING vs DEEP LEARNING
Adapted from: https://www.scs.org.sg/articles/machine-learning-vs-deep-learning
# 3

## Slide 4
OVERVIEW OF NEURAL NETWORKS
…
x1
x2
x3
a1
a2
a1
a2
y1
y3
y2
X
A2
AL-1
AL
Neural network
w1
wL-1
Notations
L = Loss function (e.g., mean squared error)
AL = Output (or activation) at layer L
X = Input features
Y = Output values
η = Learning rate
L(w)
Non-linear due to the incorporation of activation functions
Backpropagation algorithm minimizes the error by updating the weights and bias terms of the neural network
Model development involves two phases: Training and Inference.
During training, we aim to minimize a Loss Function that measures how well a prediction (ŷ) matches the actual outcome (y). Once the model has been trained and its parameters optimized, it is used to make predictions on new, unseen data.
# 4
Notes: The backpropagation algorithm uses the gradient descent optimization method to update the weights and biases of the network. The gradient descent method calculates the gradient of the error function with respect to the weights and biases, and then updates the weights and biases in the direction of the negative gradient, which reduces the error.
gradient descent is used to optimize the loss function by iteratively adjusting model parameters to minimize the loss,

## Slide 5
ML Forecast Product for IVT prediction out to 7 days; Forecasts issued throughout the water year (https://cw3e.ucsd.edu/ml_forecasts/)
Chapman et al., (2019)
5-20 % less error than GFS in predicting AR intensity at 1-7 days lead time
RMSE [kg m-1 s-1]
0-168 hr prediction of IVT for Atmospheric Rivers (ARs)
ML Method: Convolutional Neural Network (GFSnn)
Training: 10 years of GFS (Oct 2008 – Apr 2016)
Testing: 1 year (Oct 2017 – Apr 2018)
Ground-truth: NASA’s MERRA-2
HIGHLIGHT #1: ML-BASED PREDICTION OF IVT IN NEAR REAL-TIME
# 5
Notes: Provided by: Agniv Sengupta/Luca Delle Monache

## Slide 6
HIGHLIGHT #2: DEEP LEARNING FOR IMPROVED FREEZING LEVEL FORECASTS
Application of U-Net Convolutional Networks for FZL Postprocessing over Yuba-Feather Watershed: Winter 2016-17
(the higher the better)
(the lower the better)
RMSE
Correlation
West-WRF
U-Net Deep Learning
Correlation
RMSE (m)
Gorooh et al., (2025), in review
# 6
15-20% forecast skill improvement with Deep Learning Postprocessing

## Slide 7
Skill Score (the higher the better)
Dec 2021 – Mar 2022
Probabilities of 24-h accumulated precipitation > 1 inch, 12 UTC, 24 Dec 2021
PRISM (obs)
GEFS
West-WRF 200-member Ens
PRISM (obs)
West-WRF 200-member Ens + Deep Learning (DL)
PRISM (obs)
West-WRF 200-member Ens
West-WRF 200-member Ens + DL
Deep learning applied to West-WRF 200-member ensemble:
Leverages the GEFS and the ECMWF to generate an improved prediction
Can be generated with short training (only a few water years used in model training)
Capable of maintaining the high probabilities while reducing the locational biases
Ghazvinian et al., (2024)
HIGHLIGHT #3: POSTPROCESSING WEST-WRF 200-MEM ENS FOR PRECIPITATION
# 7
Key takeaway: 10-15% QPF skill improvement with CW3E 200-member ensemble + Deep Learning
Notes: 4 months of traiing

## Slide 8
Predictive skill of ensemble
Predictive skill for precipitation exceeding specific thresholds
(the higher the better)
(the higher the better)
(the higher the better)
HIGHLIGHT #3: WEST-WRF 200-MEMBER ENSEMBLE + DEEP LEARNING:
PERFORMANCE FOR 25 DEC 2022 - 18 JAN 2023 FOR FAMILY OF 9 ARs (CALIFORNIA)
Key takeaway: 3-day lead forecast skill from West-WRF+DL as good as 1-day lead forecast skill from ECMWF Ensemble/GEFS
# 8
Ghazvinian et al., (2024)
Notes: 60 days of training

## Slide 9
HIGHLIGHT #4: AI DATA-DRIVEN MODELS
Key Takeaways :
Recently, AI-enabled weather models have emerged as a cost-effective option for meteorological forecasting
Once trained, it takes seconds to minutes to produce a 4D, multivariate, 10-day global forecast
Demonstrate similar performance to ECMWF’s IFS at weather time-scales (< 7 days)
Baño Medina et al., (2025a)
# 9

## Slide 10: PROGRESS OF AI WEATHER MODEL SKILL OVER TIME
AI model forecast skill improvement over time
How does this translate to FIRO benefits at the regional scale?
Publication Year
Source: Stephan Rasp GitHub
#10
(the higher the better)
Notes: Chart shows the progress of global AI-weather models over time, for 500hPa geopotential (Z500). The purpose of these isn’t to provide an exact scoring of which model is best but rather to give an overview of the overall progress of the field.
3 day scores are chosen to minimize the potential confounding effect of blurring on RMSE metrics (at 3 days HRES RMSE is roughly equal to ENS mean RMSE).

## Slide 11
(a) AI Ensemble Generation Strategy
A 540-member AI-based ensemble (EnAFNO) of neural weather models is developed for the prediction of extreme events.
#11
HIGHLIGHT #4a: AI LARGE ENSEMBLE FOR PREDICTION OF EXTREME EVENTS
Baño Medina et al., (2025a)
(b) Evolution of TCWV for Oroville Dam AR Event
.
.
.
Individual ensemble members
ERA5 (ground-truth)
AI model skill at par with or outperforming state-of-the-science physics-based models.
Forecast generation with AI models takes secs-to-mins with significantly less energy.

## Slide 12
HIGHLIGHT #4b: APPLICATION AS CLIMATE ATTRIBUTION TOOL FOR EXTREME ARs
Total Column Water Vapor (TCWV) over the Feather River basin
Baño Medina et al., (2025b)
#12
Key Takeaways :
Depict a larger range of possible outcomes compared to dynamical model
Better representation of extreme events with significantly larger number of ensemble members
Apply AI models as climate attribution tools in real-time to quantify human footprint on intensity of extremes
2017 Oroville Dam Extreme AR Episode

## Slide 13
Highlights of CW3E’s AI-6km weather model:
87 variables at 13 vertical levels
6-hr temporal resolution
Training datasets: CW3E’s 40-year reanalysis (available at 2-km and 6-km resolution) and ERA5 (N320 config)
Pressure level variables include z, temp, u and v winds, specific humidity.
Single-level variables: MSLP, 2-m temp and dewpoint temp, SST, IWV, IVT, and winds.
AI model: Graph Neural Network (GNN) leveraging ECMWF’s Anemoi framework
HPC: NCSA’s DeltaAI (64 H100 GPUs)
Weeks to train, but minutes to predict!
Stage A: Global model
Stage B: Stretched-grid model
HIGHLIGHT #4c: A REGIONAL HIGH-RES AI WEATHER MODEL FOR WESTERN U.S.
Baño Medina et al., (2025d), in review
#13

## Slide 14
  Key Takeaways:
Reduces QPF errors over the Western US
Outperforms global models (i.e., IFS)
Effectively captures extreme precipitation events, particularly those linked to ARs.
Performs competitively with the regional NWP model (West-WRF)
Orders of magnitude faster for real-time forecast generation (only 6-mins to generate a 7-day forecast on a single GPU)
HIGHLIGHT #4c: REGIONAL AI MODEL FORECAST SKILL RELATIVE TO BENCHMARKS
Baño Medina et al., (2025), in review
Forecast skill as a function of spatial window size (top) and precipitation thresholds (bottom)
#14
(the higher the better)

## Slide 15
Integrated Vapor Transport (IVT, kg m-1 s-1), for a 7-day prediction of the 2022 New Year’s Eve Atmospheric River
Ground-truth (ERA5)
CW3E’s AI Model
THANK YOU!
Contact:
Agniv Sengupta, Ph.D.
CW3E Machine Learning Team Lead
Scripps Institution of Oceanography
University of California San Diego
Email: agsengupta@ucsd.edu

## Slide 16: BACK-UP SLIDES

## Slide 17
NEAR REAL-TIME FORECAST PRODUCT GENERATING PROBABILISTIC QPFs
https://cw3e.ucsd.edu/ml_forecasts/
Associated near real-time (NRT) forecast product generating probabilistic QPFs operationally throughout the water year
Model outputs include ensemble mean and ensemble spread in 24-hour accumulated precipitation, in addition to probabilities of exceedances of various thresholds (>1mm, >10mm, >25mm, >50mm, >100mm).