## Slide 1: Leveraging Ensemble Forecasts & Model Predictive Control to Support FIRO Projects
Kyla Semmendinger-Raney, Mahdi Erfani, Abdul Moiz, and Rob Hartman
Water Resources Engineering, Center for Western Weather and Water Extremes,
Scripps Institution of Oceanography, University of San Diego
Notes: 15 minutes
Target: 12 minutes / 3 minutes for questions

## Slide 2: Leveraging Ensemble Forecasts & Model Predictive Control - Summary
Key Topics | Key Takeaways
Model predictive control (MPC) as a FIRO strategy Can leverage deterministic (MPC) or ensemble forecast information (tree-based MPC) Scenario reduction for computation time Assess at Prado Dam to balance flooding and water conservation for groundwater recharge | Provides real-time decision support for reservoir operations Tree-based MPC leverages spread in ensemble to improve release decisions over a deterministic forecast Scenario reduction reduces computation time without degrading value of forecast Case study at Prado reduces flooding outcomes and increases post-event water storage

## Slide 3: Forecast-Informed Reservoir Operations
Seems intuitive that reservoir operators could benefit from improvements in weather and streamflow forecasts
Leveraging forecasts in reservoir operations is complicated by:
  System complexity
    Forecasts aren’t easily integrated into existing operations
  Operational constraints
    Systems must meet strict upstream and downstream flow requirements
  Forecast uncertainty
    Ensemble forecasts can increase policy complexity and computation time
How can we leverage ensemble forecasts to improve reservoir operations without violating operational constraints?
Notes: - there have been so many advancements in weather and streamflow forecasts, it seems somewhat intuitive that water managers could benefit from these forecasts to improve reservoir operations.
- however, there are a few factors that complicate actually leveraging these improved forecasts to improve reservoir operations
- including system complexity and strict operational constraints that water managers must adhere to which may limit the value of forecast information
- even if the first two were completely addressed, at the end of the day, any forecast is going to be uncertain. ensemble forecasts are great to represent uncertainty and the spread of plausible outcomes, however they can increase the complexity of a control policy as well as computation time.
- Given all of these challenges, we're really interested in exploring how we can leverage ensemble forecasts to improve reservoir operations in a way that's computationally feasible and adheres to strict operational constraints?

## Slide 4: Model Predictive Control
Notes: to do this, we've been testing a control theory called, model predictive control, or MPC
MPC is a real-time decision support tool that makes use of a model of the system to simulate the expected system state and objective function performance, given some forecast trace.
at some time, t, we have a forecast of some horizon, h, of daily inflows
at each of those days, let’s say our objective is to meet some storage threshold
so for each day over the forecast horizon, given some inflow and initial system state, there is a release we could make that gets us close to or near the ideal storage trajectory.
here, we optimize the release decisions over the FULL forecast horizon to minimize our objective, BUT we only implement the first day's release
then, we step forward a day, we look at the observed inflows, the actual release, and the observed storage all of which may differ from our forecasted values.
we use the observed values to update our initial conditions.
and then we repeat the same process for the next day with the updated forecast and keep stepping forward in time day by day
this is fairly straight forward with a single forecast trace, like a deterministic forecast, but we have to expand this slightly to leverage ensemble forecasts

## Slide 5: Tree-Based Model Predictive Control
Notes: this is where a specific formulation of mpc comes in, called tree-based mpc
Just like the example before, we have some inflow forecast. However, now we have multiple traces all stemming from the same point, today.
One optional step in TB-MPC is scenario reduction, which can help reduce computation time. Which basically groups similar ensemble members, keeps a single member to represent that group and aggregates the members' probabilities into the remaining member.
Then with our reduced ensemble forecast, we can format the ensemble members into a tree-like structure. Starting at the first day, and moving through the forecast horizon, and introduce branching points where the members become distinctly different from one another. and we do that over the full horizon until we have our complete scenario tree.
Just like before where each of our inflow points had some optimal release associated with it each day. each of the branching points here, has some optimal release but
We still only have a single release to implement today. and the major point for all of this is that the release we make today has been optimized taking into account the full spread of uncertainty in the scenario tree

## Slide 6: Prado Dam
Santa Ana River near Los Angeles, California
Operational considerations:
  Upstream flooding at 514’ reservoir elevation
  Downstream impacts at releases > 5,000 cfs
Primary operating objective is flood control
  Water storage for groundwater recharge
1998 flood event (2/9/1998 – 3/3/1998)
Compare releases for:
  Existing operations (baseline)
  MPC with perfect forecast
  MPC with deterministic forecast (ensemble mean)
  TB-MPC with ensemble forecast (HEFS)
Notes: to test the value of MPC, we use Prado Dam, located in southern California.
There are some operational considerations we need to meet,
Primarily, we need to minimize flooding, which begins to occur at a reservoir elevation of 514'.
And secondly, if there's no risk of flooding, we want to maximize water storage for groundwater recharge. Here, holding water and releasing it slowly is better to maximize the water that's actually percolated.
For this analysis, I'll show simulations from the 1998 flood event. Where all scenarios start from the same initial conditions.
And we compare the flooding/water storage between existing operations, which I'll refer to as the baseline. Then 3 formulations of MPC. MPC with perfect insight, MPC with the mean-of-the ensemble to represent a "deterministic" forecast. both of those formulations are a single forecast trace and single trace of optimized releases. and then TB-MPC with a reduced set of HEFS ensemble forecasts, developed by the National Weather Service.
I’ll also note that this is an interesting event because there were smaller storms leading up to the peak inflow in late February. So our simulation period includes those blips to see how the scenarios manage a flood in an already wet system

## Slide 7: Results from the 1998 Flood Event
95th percentile
Notes: like i mentioned earlier, mpc simulates conditions over the forecast horizon for each day that a release decision is made. so looking at the first day of our simulation period,
here is what the scenario tree of the ensemble forecasts looks like.
And the black line shows the 95th percentile of observed flows, so anything above that line is a pretty large event
The optimization finds a sequence of releases that tries to balance our two objectives: flooding and groundwater recharge.
So we’d implement the release decision for today.
Then we use the observed inflows,
since our forecasted inflow and observed inflow were pretty much the same, our forecasted storage ends up being pretty close to what actually occurs in the system.
next, we re-initialize our system and keep marching through the full simulation period

## Slide 8: Results from the 1998 Flood Event
Flooding
Notes: so to compare our 4 reservoir operating strategies.
Here are the observed inflows over the full simulation period.
And the releases over that period for each of the 4 scenarios.
the baseline existing operations is in black, mpc with a perfect forecast in yellow, tree-based MPC in orange, and mpc with a deterministic forecast in red
And you can see that all MPC runs start releasing water in preparation about 1-2 days before the baseline does. And on the tail end, the MPC formulations taper down releases after the peak to retain water. MPC with a perfect forecast does so a bit more aggressively since there is no longer a storm signal over the forecast horizon.
when we look at storage over the simulation period, we see a pretty interesting story. the mpc with a deterministic forecast results in roughly the same flooding outcomes as baseline operations. however, tb-mpc is able to achieve essentially the same flooding reductions as a perfect forecast. reducing flooding magnitude and duration.
and post-flood peak, the perfect forecast operations are able to hold on to the most water. and the MPC operations with the ensemble forecast and deterministic forecast were able to save about half the amount of water.
to put it into perspective, this additional storage is equal to about 4 weeks of groundwater recharge and around 2 weeks of groundwater recharge for the tree-based and deterministic mpc operations.
which is pretty exciting given these are results from just a single flood event.

## Slide 9: Conclusions and Future Work
MPC increases leftover storage without increasing flooding
  TB-MPC leverages uncertainty in ensemble forecast to reduce flooding
Benchmarks show MPC is viable to provide real-time information for water managers
Next Steps
  Scenario reduction sensitivity analysis
  Simulate synthetics for Seven Oaks PVA
  Incorporate into virtual FIRO operations
Source: Brodeur et al. 2024 (10.1029/2023WR034898)
Notes: all of the MPC operations were able to identify solutions to increase post-event water storage without increasing flooding outcomes
and the tree based mpc was able to leverage uncertainty in the forecast to closely emulate perfect forecast operations
this is all great, but we're talking real-time operations, so if the optimization takes days to converge, it's not really useful for decision makers that need to make decisions now. but our Preliminary benchmarks show that mpc is computationally efficient to provide real-time information for water managers especially utilizing scenario reduction.
there's a lot of work that we want to continue with
first is a more formal sensitivity analysis on the scenario reduction algorithm. really to get at how much we can reduce the HEFS forecasts before we see degradation of performance
next is to expand this to the full period of record, which is about 30 years to see how water is managed for a much longer period rather than for a single flood event.
and lastly is to integrate MPC into virtual operations. currently, CW3E provides water managers at prado dam with real-time information using the operational ensemble forecasts various forecast informed operating strategies. so we'd like to get MPC on the website to given water managers even more information to hopefully help them manage their systems as efficiently as possible.

## Slide 10: Questions?
ksr@ucsd.edu

## Slide 11: Supplemental Slides

## Slide 12: HEFS vs Reduced Scenarios
HEFS Forecast – Issued: 2/9/1998
Reduced Set of HEFS Forecasts

## Slide 13: Reduced Scenarios vs Scenario Tree
Reduced Set of HEFS Forecasts
Scenario Tree from Reduced HEFS

## Slide 14: Results from the 1998 Flood Event
Notes: and we do this over the entire simulation period.
so here is what the ensemble forecast looks like, and the subsequent optimized release and storage trajectories, with the black lines showing the observations for each.

## Slide 15: Scenario Reduction Algorithm
Notes: (Gröwe-Kuska et al. 2003)

## Slide 16: Scenario Tree Generation

## Slide 17: Optimization Details
Optimization:
  NSGAII
  DVS: 15 (MPC-Perfect), 15 (MPC-Det), 120 (TB-MPC)
  NFE: 200,000
  Objectives:
    Minimize magnitude of exceedances over reservoir elevation of 512’
    Maximize groundwater recharge
Constraints applied on final optimized release:
  Max release schedules, max IROC, min environmental flow, min downstream flow

## Slide 18: Pareto Front Policy Selection
If reservoir elevation >= 512’:
  Pick best policy for flood control
If reservoir elevation >= 510’ and 5-day forecast >= 95th inflows:
  Pick policy for 80% flood control, 20% storage
If reservoir elevation < 510’ and 5-day forecast >= 95th inflows:
  Pick policy for 70% flood control, 30% storage
Else:
  Pick best recharge policy

## Slide 19: HEFS vs Reduced Scenarios (2010)
15%
9%
12%
30%
34%

## Slide 20: Reduced Scenarios vs Scenario Tree (2010)
15%
9%
12%
30%
34%