## Slide 1: Developments in Ensembles Capabilities for EVALUATION OF FIRO ALTERNATIVES
Evan Heisman, PE
USACE Institute for Water Resources
Hydrologic Engineering Center
HEC-WAT Team Lead

## Slide 2: WHAT IS HEC-WAT?
  “Watershed Analysis Tool”
  Model Integration
    Desktop application with Distributed Compute option
    Plugin Architecture
    Supports HEC programs, easy to extend to others
  Event-based Monte Carlo simulation
    Separate natural variability from knowledge uncertainty
    System-based approach
Hydrology
Reservoirs
Hydraulics
Individual events, many times over
Notes: Notes in BOLD NOT ON SLIDE
Desktop application w/ Distributed Compute option (in comparison to FFRD, which is cloud-first)
System-based Risk Analysis: jointly modeling hydrology, reservoir operations, hydraulics, and impacts in one simulation; develop common watershed model across H&H/FRM team members
  Informed by ER 1105-2-100 Planning Guidance Notebook; ER 1105-2-409; ER 1105-2-101 Risk Assessment for FRM studies; EC 1110-2-6067 USACE process for NFIP Levee
  Example applications: modeling system-wide interactions between
    landscape changes to hydrology (e.g. wildfire or urbanization impacts on FRM);
    reservoir operations proposals
    structural changes to FRM projects
    Non-structural measures in flood impacts
  Integrates existing HEC software (HEC-HMS,HEC-ResSim,HEC-RAS,HEC-FIA) with a plugins approach; so other models can be pulled into WAT
  Allows use of existing models or sharing models with CWMS (or at least gives a good starting point that modelers are familiar with; can reduce data collection needs and initial model calibration; additional changes to adapt between studies and real-time models necessary
‘Monte Carlo’ simulations to separate modeling of natural variability from uncertainty - repeatedly simulate the system while varying inputs (boundary conditions) within expected probabilities to compute risk and uncertainty
Has been applied to watersheds from small drainages up to scale of Columbia and Missouri River. for GI studies, WCM updates, regulated flood frequency determinations, and climate change impacts to reservoir operations Beta 1.1 version just released this spring!

## Slide 3
Peak Flow (cfs)
Exceedance Probability
1
0
Stage (ft)
Flow (cfs)
Stage (ft)
Damage ($)
Computing EAD with Monte Carlo Simulation
using an “event sampling” approach
choose random flow event
replace flow-frequency curve with a random sample…
Damage
one event
…end with a sample of damages
Damage ($)
Relative Frequency
CDF
Notes: We switch the problem to a Monte Carlo simulation by replacing the flow frequency curve by a large sample of values from it. This is called an “event sampling” approach. Reflecting through the other summary relationships produces a value of damage for each flow, ending in a sample of damage. The sample average is an estimate of the EAD.

## Slide 4
Damage ($)
Relative Frequency
Peak Flow (cfs)
Exceedance Probability
1
0
Reservoir Analysis
Channel Hydraulics
Levee Behavior
Spreading Model
Inundation Mapping
Structure Inventory
Damage to Structures
Damage
one event
hydrographs
stages
damages
Using models rather than simple transforms
WAT/FRA replaces transform curves with models
random flow events
replace flow-frequency curve with a random sample…
…end with a sample of damages
REALIZATION
CDF
We don’t have to replace ALL transforms with models, just the complex ones
Flood Risk Analysis
Notes: We use the event sampling Monte Carlo approach to allow us to replace the simple summary relationships with more careful modeling of each generated flood event.
The sampled flow is turned into a hydrograph (based on a randomly chosen shape), and routed through a reservoir model (with a randomly chosen starting pool). It then goes through a channel model to see if stage exceeds a randomly chosen levee breach height, and a spreading model if breach occurs. Next, inundation is mapped and compared against a structure inventory to determine damage to structures.
The resulting sample of damages is more carefully formulated than the version that depended upon summary relationships.
When the system being modelled is a watershed, rather than a single index point like this, there are further benefits to this approach. Flows can be provided for various streams, and damage areas at confluences, that can be inundated by each reach, will show inundation by one side or the other or both at the appropriate frequencies. Another benefit is upstream levees. If a levee breaches, and thus decreases the flow volume below it, the lower system will show that lower flow against its levees and damage areas.

## Slide 5: Regulated Frequency Curves
unregulated
regulated
initial frequency curves without uncertainty
unregulated
regulated
uncertainty in unregulated frequency curve
- must propagate it to regulated
90% confidence interval
Normal probability axis

## Slide 6: Regulated Frequency Curves
one realization – the inner loop of the MC
Normal probability axis

## Slide 7: Regulated Frequency Curves
10 realizations of regulated frequency curves
Normal probability axis

## Slide 8: Regulated Frequency Curves
90% confidence interval from 100 realizations
& best estimate curve
Normal probability axis

## Slide 9: Evaluating of FRM CHANGES TO Reservoir Operations for FIRO
Assessment of flood risk = probability x consequences
  Ultimately need to assess consequences, but as a screening tool, changes in regulated flows or pool elevation frequency may be useful
Modeling for FIRO may be limited to reservoir operations if the only proposed changes are in operations.
Need to run many events and permutation of events to capture probability:
  Combinations of:
  - inflows to the system,
  - forecasts
  - initial reservoir content

## Slide 10: Prado Case Study
Case Study used to develop:
Prototype of Synthetic Forecasts
Development of Forecast Processor Plugin
Evaluated with Simplified Forecast Operations (SFO) techniques
We did not complete a full HEC-WAT Monte Carlo simulation with the Case Study; did not get final FVA operations
Notes: SFO techniques – using metrics derived from forecasts to determine reservoir operations; such as relating 3 day inflow forecast at a particular probability to the release required. Differs from EFO in that individual ensemble members do not need to be regulated to determine the release.

## Slide 11: Generalized FIRO Model Sequence
General process for using HEC-WAT with forecast ensembles
Hydrologic Sampler: random, synthetic hydrologic event
Ensemble Forecast Generator: synthetic stochastic ensemble forecasts for event (skill derived from hindcast ensembles)
Ensemble (Forecast) Processor: computes probability metrics from ensembles
HEC-ResSim operates based on metrics and Hydrologic Sampler event
Another Potential: HS generates precip, HEC-HMS generates hydrographs; SynFcsts around them, HEC-ResSim for operations, w/ output passed to other models (HEC-RAS/HEC-FIA) for consequences or and other performance metrics
Hydrologic Sampler
HEFS Data (hindcast) and parameters of stochastic ensemble model
Ensemble Forecast Generator
Randomly Generated Events
User Specified Settings
Ensemble Forecast Processor
Synthetic Ensemble Forecasts
Randomly Generated Events
HEC-ResSim
Probability Metrics
next model in sequence
CWMS does this

## Slide 12: Some Logic for Reservoir Decisions with Uncertain Info
When lead time is longer, smaller actions have more effect (lower release)
The smaller the action, the easier it is to reverse if the forecast changes
Shorter lead time requires higher release to evacuate the same volume
When must be confident that the volume won’t be GREATER than X, use a high percentile, e.g. 98%ile
  E.g., Defining releases to prevent filling the reservoir (uncontrolled release)
When MUST be confident that the volume won’t be LESS than X, use a low percentile, e.g., 10%ile
  E.g., Drafting conservation volume

## Slide 13: Synthetic Forecast Generation
(Using process developed by Cornell University, Dr Steinschneider + Dr Brodeur)
Objectives:
- Effect of forecast error on regulation of flood events to quantify uncertainty in FRM operation
- “Robustness testing” of FIRO operations -> consistency of other benefits
Notes: Ongoing collaboration with FIRO Team (Cornell University, Dr Steinschneider + Dr Brodeur)
Objectives:
- Evaluate effect of forecast error on regulation of flood events to quantify uncertainty in FRM operation
- “Robustness testing” of FIRO operations
Method:
- observed - hindcast -> “skill” – statistical properties of forecast error
- sample forecast errors from skill + “observed” hydrograph -> forecast hydrograph
Can be applied to synthetic hydrology, scaled or generated from a rainfall-runoff model.
OR create many new sequences of forecasts across entire POR
Concerns: consistent development of hindcasts w/ representative skill is costly
future: work with HMS teams to generate hindcasts with their ensemble computes
Forecast skill sampling is still just a model; we hope that real forecasters do better than the hindcast, and that reservoir operators are more aware of weather forecasts and possible outcomes than the forecasts and operations in a studies model
SynFcst will be useful in studies even with HEC-HMS as it could reduce computational burden when focused on FRM impacts and robustness testing – derive fcst skill from a HMS ensemble forecast, then apply to synthetic hydrographs from HMS.

## Slide 14: Caveats and Challenges FROM CASE STUDY
Synthetic Forecast Generator in WAT only tested on Prado with a single forecast location
  HEC plans to support districts implementing this on more locations
Hindcast dataset:
  available at all necessary locations
  representative of forecast skill across the whole range of flood events
  forecast skill / sources of error are not changing over time (stationarity)
- Ensemble Forecast Processor in WAT still needs better UI from CWMS version

## Slide 15: Output Metrics
WAT Results can inform many different metrics
FRA (Monte Carlo) compute:
    Peak outflow for flood risk management performance,
    Peak pool elevation for dam structure loading, impacts on upstream inundation.
Deterministic POR compute
  (or synthetic PORs)
    duration analysis on regulated flow:
      conservation of water benefits, ecosystem benefits
    Timing, duration of increased pool elevation for impacts in reservoir pool (recreation, ecosystem)
    volume / timing of water delivered annually
Other metrics / analysis a study could consider:
    Resilience/robustness to forecast error
    Flood Risk / frequency of consequences

## Slide 16: OUTPUT METRICS – ASSESSING OPERATIONS
Ways to be wrong with the forecast -> impact to reservoir operations
  FRM: Captured too much of a flood, or did not reserve enough space
  Increased downstream flows above channel capacity or other threshold
  Increase in peak pool frequency above allowable FIRO operation
  Spillway activation
Other impacts: Failed to capture a flood event
  Compromising chance to refill reservoir ->
    lower storage after an event or at the end of flood season
  Late (or early) timing of releases. ->
    relative difference in unregulated to regulated peaks
Compare paired sets of flood events on two (or more) alternatives
  A more robust alternative should have less uncertainty in the regulated flow.
  Robustness testing might not require as large of a compute as a proper determination of flood risk, could be done earlier in the evaluation of alternatives.