## Slide 1: Quantifying Seasonal Snowpack Water Storage for Reservoir Operations
Wyatt Reis and Shad O’Neel
Siobahn (Nani) Ciafone, Sydney Baratta, Julie Parno, Mike Bartles, Mark Robertson, Micah Johnson, Micah Sandusky, Jeff Deems
Cameron Pass, Colorado
Lucky Peak Dam, Idaho
Wyatt Reis, PE
Research Civil Engineer
Wyatt.K.Reis@usace.army.mil
Notes: Introduction, collaborators, thank you for opportunity to present
the variability is snowpacks is critical to understand for water resources, hydro power, and flood risk.
Highlight variability in both pictures, the changing landscape with the wildfire.

## Slide 2: Seasonal Snowpacks – Our Largest Reservoir
Of the 21 largest reservoirs in the western U.S. (storage capacity greater than 1.6 million acre-feet), 67% of the storage is from snowmelt.
-Li et al., 2017
Li et al., 2017
Snowpack store water during the cool season and releasing water gradually throughout the warm season.
Notes: Snow is our largest reservoir in the western US. The lag in water release.
How important it is for streamflow ~70% of streamflow in the western US.

## Slide 3: Risks Associated with Seasonal Snowpacks
Snow drought during water years 2014 and 2015 in the western U.S., particularly California.
  Total statewide costs of $4.9 billion.
-Howitt et al., 2014, 2015
Rain-on-Snow flooding in California (2017) and the Greater Yellowstone Area (2022) both resulted in significant damage and economic losses over $1 billion dollars.
Giovando et al., 2025
Huning et al., 2020
Notes: Due to the importance of snow to water resources, snow droughts have grave impacts on economic drivers, particularly agriculture. Need to lease/buy water.
Also flood risk, high snow years (2017 in CA), can also result in ROS. ROS is occurring further in land. More widespread with changing precipitation phase patterns, snow levels.
Truckee river flooding in 2017.

## Slide 4: Uncertainty in Measuring Seasonal Snowpacks
Uncertainty in snow water equivalent for the western U.S. is somewhere between 1-5 times the volume of Lake Mead.
-Steve Margulis, UCLA
If R&D can decrease water supply disruptions by 15 percent through more effectively
managing drought and improving understanding of snowpack and snowpack processes,
the annual benefit could be $1.14 billion.
-Report to USACE on the value of R&D, CDM Smith, 2023
Notes: Snow research is a 100-year-old science and while operational solutions are being developed, the uncertainty in snow water resources is substantial.
This uncertainty leads to vulnerability and by not having a strong estimate of our snowpack reservoir, we are incurring costs to our management systems, economies, and communities.

## Slide 5: Key Questions in Snow-Dominated Watersheds
How much water is stored in the snowpack?
How fast will the snow melt?
When is the water needed?
How do watershed characteristics, landscape scale changes, and meteorological conditions alter snowmelt runoff timing and quantity?
  Subsurface exchange
  Evapotranspiration, sublimation, soil moisture
  Drought, wildfire, insect endemics, rain-on-snow events
ASO and M3 Works
Notes: Here are the questions that come out of the uncertainty that exists in our understanding of our snowpack reservoir.
Walk through the graphic, explain the difficulties with the SNOTEL sites and how they vary significantly from the ASO curve, they also vary through the year in representativeness.

## Slide 6: Difficulties Forecasting in Snow-Dominated Watersheds
Snow is highly variable in space and time
  Snow climate and topographic settings are highly variable
  Historic patterns may not be useful
Improved understanding requires multi-scale, multi-sensor integration, and data-informed model developments
ASO and CA DWR
Integration of existing & new forecast systems and data
Physical snowpack & hydrology modeling
Expanded ground station networks
Notes: Historically, there has been a reliance on previous years to understand the snowpack volume and melt conditions. Changes in landscape and greater interannual variability makes these comparisons less useful.
Need for a cost–effective, multi-scale, multi-sensor, multi-model solution
No silver bullet! SNODAS does not work everywhere.

## Slide 7: Improving Measurement Capabilities
Snow depth mapping using lidar combined with station or point density to develop distributed SWE product
  Full-basin inventory from airborne platforms (ASO)
  Sub-watershed scale using helicopter and drone
However, need to address snowpack reservoir volume quantification across the U.S.
ASO Snow Depth
Elk Range, Colorado
April 2019
Butte SNOTEL
Schofield Pass SNOTEL
Notes: aerial lidar can map the snow depth over large areas with high accuracy. Highlight the variability in snow depth.
Lidar is now an operational tool with programs in the US and Canada. ASO is flying extensively in CA and CO. USACE CRREL has flown the upper Boise River (Mores Creek) watershed the past 3 years.

## Slide 8: Existing Modeling of Snow Water Equivalent
American River Basin
Pit at Shasta Lake River Basin
California Cooperative Snow Surveys Program, Model Dashboard
How do we know how much SWE is in a watershed?
  American River Basin – ASO flights are the authoritative reference
  Shasta – high variability with no known answer
Ingesting snow depth measurements, how much better of an answer are we getting?
Notes: Point out the high variability in SWE in the Shasta and American.
ASO data in the American informs volume of SWE in the American snowpack reservoir but much greater uncertainty in the Shasta. Which or any right in the Shasta?
Need to ingest data into the models, but what does this data look like. When? How? Cost?

## Slide 9: Constrain Uncertainty in Snow-Dominated Watersheds
Meteorology
Spatial and temporal observations
  Air temperature
  Precipitation quantity & phase
  Energy fluxes (radiation and turbulent fluxes)
  Solid precipitation interactions with terrain and vegetation
Weather forecasting
  Short- to medium-term conditions
Snowpack
Spatial and temporal observations
  Snow depth
  Density
Snowpack model physics
  Forcing data
  Calibration data
  Snowpack evolution
    Redistribution
    Sublimation
    Melt rate
Streamflow
Watershed characteristics
  Soil moisture
  Evapotranspiration
  Groundwater recharge
  Non-stationarity
    Wildfire
    Drought
    Insect mortality
Snowmelt duration
  Meteorology
    Rain-on-snow
Hydrology model physics
SWE

## Slide 10: Needs for Improving Snowpack Initial Conditions
  Address operational needs for flood control and water supply forecasting
    Quantify operational improvement (uncertainty)
    Data collection approaches
    Data ingestion approaches
    Identify/develop novel approaches for model improvement
      Machine learning for snow depth and density
      Data assimilation
    Mature novel metrics to identify and compare model skill.
  Obtain actionable outcomes – constrain snowpack initial conditions and snow melt processes for runoff modeling.
  Scale experiments by varying watershed size, snow regime, and meteorological and landscape conditions.
Operations
Research
Alignment of operational needs with research capacity.
Operations to Research to Operations Framework
Notes: Need for a collaborative research development (O2R2O) – operations needs to drive the research so that it is useful and usable. Applied research.
Obtain actionable outcomes with quantifiable operational improvement

## Slide 11: Value in Accurate Snowpack Measurement and Modeling
energy.gov
Operational resilience & reliability:
Minimize runoff forecast uncertainty
Optimized/increased hydropower
In-stream flow reliability
Groundwater recharge
Avoided costs:
Reducing/avoiding flood impacts
Unforeseen curtailment or water leasing
Water temperature & quality impacts from low flows
Effective policy implementation:
Measurement and modeling is fundamental to planning
Equitable & effective response to shortage
Proactive water management
Wildfire planning & response
Notes: By spending the effort on snow, we are decreasing the uncertainty and maturing operational tools that will allow us to reduce risk and reduce cost.
Not investing in snow is more costly than it is to address the issue.