## Slide 1: Seasonal Streamflow Forecasts in the Truckee FIRO Approach
Caleb Erkman, P.E. Kara DiFrancesco, PhD
cerkman@uswm.org kdifrancesco@usbr.gov
US District Court Water Master’s Office Bureau of Reclamation
Lahontan Basin Area Office

## Slide 3: Truckee Basin Overview
73% of Annual Runoff comes from snowmelt*
Seven California reservoirs  primarily Nevada use
  Prosser, Boca and Stampede – USBR-owned; flood control, water supply, environmental
  Martis – USACE-owned; flood control, inactive
  Lake Tahoe – USBR-owned; water supply
  Donner and Independence – private; M&I
USACE 1985 Water Control Manual (WCM)
  Regulates flood control to protect Reno-Sparks
  Basin-led FIRO Viability Assessment (2024)**
  USACE WCM Update initiated, expected 2028
* Li et al (2017)
** https://www.usbr.gov/watersmart/bsp/completed.html
FIRO focus

## Slide 4: Snow, Floods, and Drought  FIRO Why and How
January 1997 Reno Floods, RGJ
2023, Reclamation
2015, Reclamation
Notes: On April 1, 2015, only 25,600 acre-feet of water was stored as snow, while, on the same date in 2023, the Basins’ snowpack held over 3 million acre-feet of water

## Slide 5: Truckee Basin Snow Driven Flooding - Summary
Provided by: C. Erkman
Key Topics: | Key Takeaways:
Rain on snow flooding Seasonal runoff Snowmelt parameter (traditional and FIRO) Variable FIRO space Spring runoff flooding Flood regulation target | Truckee Basin benefits from a long snowpack record, skilled forecasts, and strong institutional knowledge. High snowpack increases flood risk and provides water supply security – FIRO aims to balance tradeoffs. In years with large seasonal runoff, FIRO encroachment can add unnecessary risk and little/no supply benefits. Spring runoff flooding is vulnerable to an overly restrictive flood regulation target  increasing the Reno flood control target can actually reduce risk.

## Slide 6: Long History (>100 years) of forecasting runoff from Snowpack
“Father of Snow Science” Dr. James Church (UNR)
  1908 invented Mt. Rose Sampler to measure snow water equivalent (SWE)
  1910 initiated snow course sampling program
  Federal Snow Sampler still used today
Many more tools available now
  SNOTEL, Airborne Snow Observatory, Remote Sensing, etc.
Quantification of SWE is basis of modern seasonal runoff forecasts
Special Collections and University Archives Department, UNR

## Slide 7: guide curves Based on Expected Snow runoff
Chart: Prosser Creek Reservoir Flood Control Diagram (1985 WCM)
1985 Water Control Manual (WCM) Snowmelt Parameter
  Spring refill curve depends on April-July runoff forecast (FIRO? firo?)
  Based on “snow-on-the-ground”, not future weather
  No refill before April 10 (historical snow forecast availability)
Variable spring refill space

## Slide 8: guide curves Based on Expected Snow runoff
Chart: Prosser Creek Reservoir Revised Guide Curve (2023)
Chart: 
700
800 kAF
900
1000 kAF
1985 Water Control Manual (WCM) Snowmelt Parameter
  Spring refill curve depends on April-July runoff forecast (FIRO? firo?)
  Based on “snow-on-the-ground”, not future weather
  No refill before April 10 (historical snow forecast availability)
Revised Guide Curves (2024)
  Earlier spring refill, based on water year (WY) runoff forecast
  Later fall drawdown
  No flood storage change
Currently operating under revised guide curves
Spring 2024 & 2025 deviations;
WY 2026-2030 request submitted

## Slide 9: Wet Antecedent Conditions  Larger Probability and Magnitude OF Floods
Flood Events: 1986 - 2019
Flood events typically happen during large snow periods
Fall flood events are rare - lack of antecedent wetness
ARkSTORM 2.0
Re-creation of the Great Flood of 1862
Wet initial condition result in ~17,000 cfs higher peak flow
  Reservoirs cannot recover fast enough
  Compounding risk from series of storms
1997 Flood
~17,000 cfs
~1997 flood

## Slide 10: Truckee basin ≈ Region with “Best” Forecast skill
Cordeira, et al (many of whom are in attendance), 2025
Lake Tahoe (16050101)
Truckee (16050102)
Notes: Cordeira JM, Ralph FM, Talbot C, et al. A Summary of U.S. Watershed Precipitation Forecast Skill and the National Forecast-Informed Reservoir Operations Expansion Pathfinder Effort. Wea. Forecasting. 2025;40(8):1529-1542. doi:10.1175/WAF-D-24-0188.1

## Slide 11: Incorporating Snow and flood information into Truckee FIRO

## Slide 12: A Little Background…
FIRO space sizing
  Multi-objective evolutionary algorithm used to determine the size of FIRO space
  Constrained to operating ≤70% of the flood space using FIRO
    Stakeholder selected pareto-optimal solution operates 70% of flood space using FIRO
Alternative operational scenario evaluation:
  Metrics: water supply, environmental flow, flood risk, and operational objectives
  Event simulations
Event simulation – 2017 water year and scaled 100-yr flood
  Record-setting snowpack, runoff, and several floods
  FIRO simulation allowed significant encroachment – stakeholders deemed unnecessarily risky
Opted to limit FIRO based on water year forecasted volume
  No significant impact to water supply or environmental flow metrics

## Slide 13: Probability of refill based on Forecasted water year Runoff
If reservoirs would refill under 1985 WCM, FIRO encroachment is an unnecessary risk
Predicting refill is a complex function of:
  Initial storage
  Future runoff
  Demands
Simplified refill prediction for FIRO based on water year flows
  WY Runoff > 600 kAF, reservoirs always filled
  WY Runoff < 300 kAF, reservoirs never filled
  WY Runoff 300 KAF – 600 KAF
    Reservoirs fill 36% of the time
    On average reservoirs reach 79% of capacity
Won’t Fill
Might Fill
Will
Fill
No added supply benefits from FIRO encroachment
Largest supply benefits from FIRO

## Slide 14: Variable Firo Space
Variable FIRO Space size based on Water Year Farad Natural Flow
  Quantitative assessment and subjective risk tolerance
  “Optimized” at 70% of Revised Guide Curve
Minimize flashy operations – limit daily change in maximum FIRO Space (<2%)
Determination of FIRO Sizing (% of guide curve flood space)
Max FIRO (70%)
Water Year Farad Natural Flow (WY FNF)
600,000 AF
300,000 AF
% Flood Space using FIRO
0%
Antecedent snowpack provides
insight into flood risk AND future runoff
Notes: WYFNF = FNF + plus forecasted median remaining FNF for the rest of the WY, rounded to the nearest 50 kaf

## Slide 15: Revised guide curves with Variable FIRO SPace
Chart: Prosser Creek Reservoir Revised Guide Curve with Variable FIRO Space
700
800 kAF
900
1000 kAF
Variable spring refill space
Variable maximum FIRO space
300 kAF WY FNF
600 kAF WY FNF
Preferred Operational Scenario allows encroaching into 0-70% of Revised Guide Curve Flood Space
FIRO Parameter and Spring Snowmelt Parameters are a function of water year runoff
500 kAF
400 kAF
Notes: 300 kAF

## Slide 16: Spring Runoff Flooding
Flooding due to spring runoff differs from winter rain flooding in several ways
  Peak flow is lower
  High flows last much longer
  Potential for minor flooding for a sustained period
  Limited ability to evacuate between runoff peaks
  Possibility of filling all the flood space without significant rain or any flood damages
  Risk of significant increase in flows if a major thunderstorm occurs during the runoff
Risk most significant with a large snowpack in a cold spring when little snow melts before sustained summer warm temperatures
 | Winter Flooding | Spring Flooding
Peak flow (1/100 yr 1-day average*) | 35,000 cfs | 10,000 cfs
2-week flow (1/100 yr 15-day average*) | 7,800 cfs | 7,800 cfs
Month flow (1/100 yr 30-day average*) | 5,000 cfs | 6,000 cfs
Maximum monthly rain** | 27.6 in | 8.3 in
*Truckee Basin Water Management Options Pilot Study—Rain Flood and Snowmelt Flood Frequency Curve Update, 2022
**Tahoe City NWS COOP Station, POR 1910-current
Chart: WY 2017 Reno regulated flow

## Slide 17: Addressing sustained flood flows By Increasing Flood Control Target
Overly conservative flood flow target
  1985 WCM indicates lack of damages below 14,000 cfs
  1985 WCM Reno flood control target = 6,000 cfs
    Accounts for development, doesn’t account for recent flood control projects
  National Weather Service minor flood level = 11,400 cfs
  2-D modeling and Truckee River Meadows Flood Authority – no damages below 7000-8000 cfs
Conservative target  flood space encroachment and longer sustained flood flows
  Baseline 1985 WCM
    Flows regulated to 6,000 cfs for ~6 weeks
    Flood space filled on 5/31
  Increasing the flood target to 7,000 cfs,
    Flows regulated to 7,000 cfs for ~2 weeks, split up
    Flood space never fills

## Slide 18
CONTACTS:
Kara DiFrancesco, PhD
Bureau of Reclamation
kdifrancesco@usbr.gov
Caleb Erkman, PE
US District Court Water Masters
cerkman@uswm.org
https://www.usbr.gov/watersmart/bsp/completed.html
Flickr/Jonathon Cook
Notes: https://www.flickr.com/photos/jcookfisher/39868105393