## Slide 1: Incorporating Current Snow State and Seasonal Streamflow Forecasts into FIRO - Summary
Key Topics: | Key Takeaways:
Challenges to incorporating seasonal forecasts in FIRO Introducing Direct Policy Search (DPS) New Don Pedro as a test bed for DPS Benefits and Data requirements of DPS Existing efforts at CW3E | DPS allows a very flexible reservoir operation which can balance multiple tradeoffs Once calibrated, very cheap computational cost and relatively easy to integrate Can use a variety of hydroclimate information, not just seasonal runoff forecasts

## Slide 2: Incorporating Current Snow State and Seasonal Streamflow Forecasts into FIRO
Abdul Moiz, Kyla Semmendinger-Raney, Mahdi Erfani, and Rob Hartman
Water Resources Engineering, Center for Western Weather and Water Extremes,
Scripps Institution of Oceanography, University of San Diego
Notes: Afternoon everyone. I'm Abdul Moiz from the WRE team here at CW3E.
I'll be talking about some of the recent work that our team has been doing to explore how we can integrate snow information or the current snow states and seasonal forecasts into FIRO.
Besides the WRE team, there are several other folks at CW3E who have also contributed to this work.

## Slide 3: Challenges of integrating seasonal forecasts with FIRO strategies
Current FIRO strategies rely on short-range weather forecasts (1–15 days) with a primary emphasis on flood control.
Seasonal forecasts enable long-term water supply planning, including drought preparedness and carryover storage.
Key Challenges
FIRO methods like EFO, MPC are computationally expensive; seasonal forecasts add further cost.
Limited ability to balance multiple objectives like flood control and water supply
Limited scalability which limits applications in multi-reservoir systems and large ensembles
Strategies are needed that integrate seasonal forecasts into FIRO while managing system complexity and balancing multiple objectives
Notes: Firstly, I want to give a brief background and highlight some of the key challenges to integrating seasonal forecasts in FIRO strategies.
[Next]
Current FIRO strategies rely in short-range weather forecasts, the primary emphasis here is flood control. In doing so, we can save water as well.
[Next]
However, seasonal forecast enable long-term water supply planning, including drought preparedness and carryover storage.
[Next]
So first key challenge to incorporating seasonal forecasts in FIRO methods such as EFO or MPC are that they are computationally expensive. They oftentimes require iterations and maybe optimization at every time step. Which could be further slow down because of the longer lead of the seasonal forecasts.
[Next]
Because of the way these FIRO strategies are design, they have limited ability to balance multiple objectives like flood control or water supply. There are ways around this. But then they also further add to the computational cost.
[Next]
If you make the problem more complex, such as multi-reservoir systems and large ensembles, then these methods may have limited scalability to such large systems.
[Next]
So, we do need strategies that can integrate seasonal forecasts systematically into FIRO while managing system complexity and balancing multiple objectives.
[Next]

## Slide 4: Direct Policy Search (DPS)
Time
Release
Reservoir Network
(operational constraints)
Policy
Approximator
Policy parameters
Historical SWE
(exogenous variable)
System Performance
Calibration
Notes: We are now exploring one technique called Direct Policy Search or DPS for short so see if it can help us tackle some of these key challenges.
[Next]
So, what is DPS?
Essentially, it is a function, with some parameters/variables, who's output is the release at a certain timestep.
So, the function is called a policy approximator and it always traditionally has certain variables such as day of the year and current pool level, because this information is needed to make a release decision.
[Next]
then we can add various exogenous variables, which we have the observations/modelled outputs for and which we think are important to make a release decision.
Such as SWE (snow water equivalent at the current timestep), seasonal forecast volume, short-range forecast volumes, storage in upstream reservoir etc.
[Next]
And then we have some policy parameters, which do need to be calibrated, but once they are calibrated, they are fixed, they don't vary in time.
[Next]
So once we have our policy approximator setup,
We can get different polcies, which give us different release decisions. these difference policies essentially have different exogenous variables used in them. for example, one could be using SWE, the other could be using forecast volumes and the last one could be using both.
[Next][Run animation]
So then, how do determine these policy parameters.
Well, we can have an initial guess and a given set of exogenous variables. Which can go into then policy approximator and then define releases in a reservoir network model. So, all the physical properties of the reservoir and all operational constraints are hard coded into this simulation model.
After running the model we can evaluate it for its performance, which would be related to its objectives (flood control, water supply and others)
And then we can iteratively modify the policy parameters, until we reach a certain balance between the objectives.

## Slide 5: Direct Policy Search (DPS)
Objective 1
(Flood control)
Objective 2
(Water Supply)
SWE only
Forecast Volume only
Both SWE and Forecast Volume
Adding more useful information to the policy approximator can lead to better system performance
Policy parameters only need to be decided once. Once the parameters are determined DPS is very efficient to apply in operations.
Operating policy function is sufficiently flexible to capture reservoir response to exogenous variables
System Performance
Balanced policy
Ideal policy
Notes: So, more on system performance.
We can setup differet metrics for different objectives. here i just show two (flood control and water supply).
So, we can have different release decision, by using different policy parameters, for a given set of exogenous variable inputs.
For example, if we use SWE only. We might get a pareto optimium like this.
If we use forecast volume only. we might get another pareto optimum which is even better than the previous one.
Using both these exogenous variables might lead to even better system performance.
[Next]
So, adding more information which we think might be more useful for reservoir operations, can lead to policy approximators with better performance.
[Next]
The strength of this method is that they policy parameters only need to be calibrated once. Once they are calibrated, they are very efficient to apply in operations.
[Next]
This is possible because these policy approximator functions have forms which are sufficiently flexible to capture reservoir response to exogenous variables.
[Next]
On these pareto optimum curve, we can identify one set of policy parameters, which can then give use one policy approximator, and one release decision.

## Slide 6: New Don Pedro Dam
(Source: TID)
Located on Tuolumne River, California
Gross capacity: 2.03 million ac-ft
Primarily provides water to Turlock and Modesto Irrigation Districts located downstream
Other uses include hydropower production, flood control, environmental flow for fishes.
Notes: We are now testing the application of this DPS method on New Don Pedro Dam in Tuolumne river basin.
It has a gross capacity of 2.03 million ac-ft and it primarily provides water to Turlock and Modesto irrigation districts located downstream.
But there are other uses which include hydropower production, flood control and other environmental objectives.
On the right hand side you can see a network diagram of the system.
There are three upstream reservoirs which also play a role in managing new don pedro dam.

## Slide 7: New Don Pedro (Existing operations) – WY2020
Releases for irrigation are made from Mar/Apr through October
Pool is maintained at 1,690 ac-ft until 27 April after which it increases to gross pool by 3 June
Notes: So, these are the existing operations from the WY 2020.
You can see the top of the conservation in gray.
Blue is the storage.
Black is inflow
Red is outflow.
[Next]
Essentially releases for irrigtation are made from Mar/Apr through October. These are governed by irrigation demands. Which is why you see this large outflow from Mar/Apr going all the way upto the end of October.
And the pool is maintained at 1,690 ac-ft until 27th April after which it increases to gross pool by 3 June.
On the top you can see seasonal forecasts, which don't seem to show a lot of inflow on April-June. So this is more of the default setting.

## Slide 8: New Don Pedro (Existing operations) – WY2023
In case a high snowmelt runoff is forecasted in B120, the top of the conservation pool is adjusted.
This new conservation pool is then used as the guide curve.
Notes: In WY 2023, the seasonal inflow forecasts, do show a large inflow due to a high snowmelt runoff.
So, the top of the conservation pool is adjusted, to cater for these higher inflow.
[Next]
This new conservation pool is then used as a guide curve
Gross pool: 830.0 (2.03 million ac-ft).
So, we want to see, whether DPS will allow better flexibility here and use information other than just inflow forecasts

## Slide 9: Benefits of using DPS
Very efficient in operation as it only needs to be calibrated once to determine the parameters of DPS
Can be used to determine relative importance of exogenous variables to guide reservoir operations
Can be used with variables other than seasonal forecasts, such as direct integration of snow states, forecast errors, upstream reservoir states and even S2S weather forecasts and other hydroclimate variables.
Once the parameters are decided, can be integrated with other tools as well
Key Requirements
Datasets on which the policy is calibrated need to be available in real-time for operational considerations.
Datasets need to be continuous and have a long period of record to facilitate calibration
Notes: So, just wanna highlight again, some of the benefits of using DPS
[Next]
It is very efficient. Only needs to be calibrated once to just determined the appropriate parameters.
[Next]
It could also help us determine which information is the most important to guide reservoir operations.
[Next]
Another benefit is that, multiple datasets can be used as inputs and they don't necessarily have to be inflow forecasts. they could just be precipitation forecasts or snow state estimates or even forecast errors or other hydroclimate variables.
[Next]
Since the computational cost is cheap, it could be easy to integrate with other tools as well.
[Next]
But there are some key requirements for this method.
The datasets which are defined as exogenous variables in the policy need to be avaialble in real-ti9me for operational considerations
And they also need to be continuous and have a reasonably long enough period of record to facilitate calibration.

## Slide 10: Current Efforts at CW3E and Next Steps
Development of a simulation model for New Don Pedro Reservoir
Develop and test DPS using the following SWE datasets as a pilot case:
  UA-SWANN (800 m, daily, WY1982-Present)
  NWM (1 km, 3-hourly, WY1979 – WY2022)
Consider differences in SWE products
Later, add seasonal forecast volumes at different lead times
Questions?
amoiz@ucsd.edu
Comparison of UA-SWANN and NWM SWE products over 40 years
Notes: I wanna close off this of the current efforts our team is making for this work.
[Next]
Right now, we are developing a simulation model for the New Don Pedro Reservoir network
[Next]
And as an initial pilot study case, we are setting up DPS using the following SWE datasets as a pilot case.
We are using UA-SWANN and outputs from the msot recent version of naitonal water model.
On the right you can see a snapshot of the dataset on Mar 01, 2021 and you can see there are some difference between the two datasets, but they show similar spatial patterns.
UA-SWANN is based on observations. Whereas, NWM is based on just model. There are differece between their spatiotemporal resolutions, but both have long and continuous records. and UA-SWANN is operational, although it lags behind by 2 days.
[Next]
There are also differences between the basin average SWE from the two products, so the NWM tends to underestimate SWE.
But it would be interesting to see how the policies perform using these difference datasets.
[Next]
Once we have the pilot case setup, we can then add seasonal forecast volumes and explore different lead times to see where we can get the most benefit.
[Next]
Happy to take questions.

## Slide 11: Supplemental Slides

## Slide 12: Overview of Direct Policy Search
(Giuliani et al., 2021)
Closed loop policy
real-time control
(MPC)
offline policy design
(DPS)
…
Evolutionary Multi-Objective
DPS
(EMODPS)
Define the reservoir release as a function of exogenous information
OP(dt, ht)
OP(dt, ht, basin state)
OP (dt, ht, basin forecast)

## Slide 13: Overview of Direct Policy Search
Radial Basis Function (RBF)
Release decision:
M = number of inputs variables (dt, ht, observation)
N = number of RBFs
K = number of output variables

## Slide 14: Multi-Objective Optimization
Objective 1
Objective 2
J1 = objective 1 (e.g. minimize floods)
J2 = objective 2 (e.g. maximize water conservation)
Use an optimization algorithm (e.g. borg) to optimize both objectives and get a pareto front
Set up the parallel version of ‘borg’ over ‘merced’. Able to take advantage of a large number of cores (tested up to 90 cores)
Get optimized values of RBF parameters (centers, weights and widths).
We can then get a release policy like OP(dt, ht, basin state)

## Slide 15: EMODPS
OP(dt, ht, basin state)
OP(dt, ht, SWEt)
OP(dt, ht, Pt)
OP (dt, ht, inflow forecast)
Deterministic short-range
Ensemble sub-seasonal
Ensemble seasonal
Parameterized function extracts information from forecast data

## Slide 16: Discussion on selection of exogenous variables