## Slide 1: San Joaquin Basin Watershed Studies
12th Annual FIRO Workshop
August 6th, 2025
© Merced Irrigation District 2022
Notes: Jim to provide introduction thoughts

## Slide 2: San Joaquin Basin Watershed Studies
Calaveras
Stanislaus
Tuolumne
Merced
Upper SJ
  Chowchilla
  Fresno
  San Joaquin
2
Notes: Watershed Studies examine the San Joaquin Basin tributary watersheds, Cal to Upper SJ.
Delineation of the watershed study area: Start with USGS HUC watershed delineates, then adjust for irrigation districts most closely associated to the reservoir and stream in the WS. Add any creeks that are also most closely associated.
Generally, each watershed study area is modeled independently for surface water operations (Cal and Stan are connected), but all of the watersheds are interconnected by groundwater.

## Slide 3: Objectives of the Watershed Studies
Assess and Quantify
Multi-Sector Vulnerability to Climate Change
Assess and Quantify
Multi-Sector Flood-MAR Adaptation Performance
Report Results from the Local-Watershed- Basinwide scale
Foundation to Support Coordination, Alignment, and Implementation
Watershed Studies
3

## Slide 4: Integrated Modeling Toolset
Basin-wide
Precipitation Runoff
Sac-SMA | Daily | Central Valley
Basin-wide
System Operations
CalLite | Monthly | Statewide
Local Reservoir Operations
HEC-ResSim | 3-Hour | Watershed
Root Zone Model
IDC | Daily | SJ Basin
Basinwide Groundwater Operations
FMSJSim (IWFM) | Monthly | SJ Basin
Local Recharge Operations
GRAT | Daily | Watershed
Local Precipitation Runoff (Creeks)
HEC-HMS | Daily | Watershed
Climate Parameters
Weather Generator | 3-Hour | Central Valley
Flood Risk Assessment
HEC-RAS | HEC-FDA | Hourly
San Joaquin Basin
4
Notes: Surface water models are generally independent from watershed to watershed
Groundwater model is shared across all watershed

## Slide 5: Integrated Modeling Toolset
Fields ranked
Crop Compatibility
Calendar
Recharge Suitability
Index
Recharge Operations
GRAT
Reservoir Operations
HEC-ResSim
Infinite WAFR
Groundwater Operations
FMSJSim
Monthly Recharge by Field
Track the Fate of Recharge Water
Daily Recharge Capacity
MAR Diversions
Conveyance / Turnout Capacities
Notes: Rework graphic to focus on Daily Recharge Capacity feedback loop between GRAT and HEC-ResSim

## Slide 6: FIRO-MAR Forecasting Tools
Synthetic Forecast Error Model
  Represents uncertainty in modeling forecasted inflows
  Based on historically observed forecast uncertainty
  Can be applied to any inflow timeseries
Ensemble Forecast Operations (EFO)
  Based on the ensemble forecast
  1-7-day risk-based release decision
  EFO is capped by operational constraints downstream
  Recalculate daily
Implemented in HEC-ResSim through an ensemble reader plug-in
6
Notes: Zach Brodeur and Scott Steinschneider
CNRFC ensemble mean forecast (2013-2022)
Synthetic forecast components
1-7-day lead​
Conditional mean (observation  forecast)​
Heteroskedasticity (larger forecasts  larger variance)​
VAR = 1 (correlation of error with previous forecast error)​
Correlated residuals (correlation of errors across leads)

## Slide 7: FIRO Space Determination
A FIRO space was developed considering the following guidelines:
Flood release volume over five-day period at downstream channel capacity
Size of the reservoir storage (gross) – 5% percent of storage
Size of the flood space – around 10% to 20% of flood space, maximum of 50%
Final FIRO Space developed through repeated simulation and testing
7
Chart: Storage (ac-ft)
Lake McClure Example
Merced River channel capacity is 6,000 cfs
FIRO Space = 6,000 cfs x 5 days = 60 TAF
About 6% of total storage
About 17% of flood space
Tested under existing and climate change conditions
FIRO Space Determination – 60 TAF

## Slide 8: Integrating FIRO and MAR at Lake McClure
Chart: Storage (ac-ft)
8
2a
2b
MAR Release in FIRO Space
Conservation Pre-Release
1
MAR + Flood Control Release
Reservoir Storage
1
2a
2b
Conservation Space
60TAF FIRO Space
Flood Space
Notes: After April, protect the FIRO carryover storage for eco operations and/or water supply.

## Slide 9: Lake McClure Flood Management for 1997 (+2°C warming)
9
Chart: Storage (ac-ft)
Chart: Inflow (cfs) | Crocker Huffman Flow (cfs)
Applied Recharge = 447 TAF

## Slide 10
FIRO-MAR Assumptions By Reservoir
Watershed ¦ Reservoir | FIRO Space | Design Release Capacity | FIRO-MAR Release Capacity (Operational + Daily Recharge Capacity)
Calaveras ¦ New Hogan | 50 TAF | 12,500 CFS | 7,000 CFS + Up to 600 (CFS)
Stanislaus ¦ New Melones | 80 TAF | 8,000 CFS | 5,000 CFS + Up to 1,975* CFS
Tuolumne ¦ New Don Pedro | 50 TAF | 9,000 CFS | 9,000 CFS + Up to 4,200* CFS
Merced ¦ Lake McClure | 60 TAF | 6,000 CFS | 6,000 CFS + Up to 1,900 CFS
Chowchilla ¦ Eastman Lake | 20 TAF | 7,000 CFS | 4,800 CFS + Up to 795 CFS
Fresno ¦ Hensley Lake | 35 TAF | 5,000 CFS | 4,000 CFS + Up to 260 CFS
San Joaquin ¦ Millerton Lake | 21.5 TAF | 8,000 CFS | 8,000 CFS + Up to 6,500 CFS
*Includes regulating reservoir re-operation as part of FIRO-MAR
Notes: NHG Capacity – 317 TAF; DNP Capacity – 2,030 TAF (6.4 times as big)
NHG Flood Capacity – 165 TAF (52%); DNP Flood Capacity – 340 TAF (17%) ( 2 times as big)

## Slide 11: Achieving Multiple Benefits Across Diverse Watersheds
Replenishing aquifers – check
Reducing flood risk – check
Diversifying benefits across multiple sectors?
  Be intentional with recharge placement
  Leverage additional supplies created by FIRO
Part 2:
11
Notes:     RMAs: GDEs, DACs, subsidence prone
    FTBs
    Shorebird habitat
    Eco-actions sustained using eco-pool account

## Slide 12: Two Distinct Flood-MAR Strategies
Streamlined Flood-MAR (“MAR 90/20”)
    Derived from diversion criteria under State Water Board’s streamlined permitting process
Integrated Forecast-Informed Resources Management (“I-FIRM”)
    Multi-sector resource management approach to integrating MAR with FIRO and expanded infrastructure
MAR-90/20
Requires partnership among local water managers and users
I-FIRM
Provides significant water supply, flood, and ecosystem benefits
Requires local, state, and federal partnership
Recharge Using High Flows
+ Reoperate Reservoirs
Provides some water supply benefits, but limited flood risk reduction
Recharge Using High Flows
12
Notes: The Flood-MAR adaptation strategies explored in this study represent expanding footprints of Flood-MAR operations that progressively deliver greater and more widely shared benefits
Streamlined Flood-MAR (“MAR 90/20”)
  The Streamlined Flood-MAR (MAR-90/20) strategy is derived from the diversion criteria under the State Water Resources Control Board’s streamlined permitting process for temporary and standard water rights for diversion of high flows to underground storage and using current infrastructure.
Integrated Forecast-Informed Resources Management (“I-FIRM”)
  The Integrated Forecast-Informed Resources Management (I-FIRM) adaptation strategy reflects a watershed-scale, multi-sector resource management approach to integrating managed aquifer recharge (MAR) with forecast-informed reservoir re-operation (FIRO) and expanded infrastructure towards sustainability and climate change resilience.

## Slide 13
How Much Flood-MAR Recharge is Possible?
*up to 55 taf additional
to Friant-Kern (Tulare basin) under I-FIRM
Calaveras
Stanislaus
Tuolumne
USJ
Merced
Flood-MAR “Useable Fields”
≈ 4x more
recharge in
I-FIRM
*

## Slide 14
Contours = change in GWLs
I-FIRM relative to Baseline
+2°C climate
Groundwater levels increases up to 85 feet.
Flood-MAR Replenishes Aquifers
Groundwater levels increase in vulnerable parts of watershed.
Calaveras
Stanislaus
Tuolumne
USJ
Merced
-396 TAF/yr
-490 TAF/yr
-387 TAF/yr
Baseline
Current
Baseline
Climate Change
I-FIRM
Climate Change
San Joaquin Basin Overdraft

## Slide 15
CALAVERAS River at Bellota
STANISLAUS River at Goodwin
TUOLUMNE River at Modesto
MERCED River at Crocker Huffman
Maximum flow over 100 years (cfs)
Baseline
Current
Baseline
I-FIRM
2050-TH
MAR 90/20
Design Capacity
Flood-MAR Reduces Flood Flows
*I-FIRM also reduces the frequency and duration of flood flows
UPPER SAN JOAQUIN River near Highway 41
Notes: Operational Channel Flood Capacity
The effective flow capacity of a river channel or engineered flood control channel that is available for safely conveying floodwaters under current, real-time conditions. This capacity reflects not only the channel’s original design but also operational factors such as sediment accumulation, vegetation encroachment, structural maintenance status, and temporary obstructions that may reduce conveyance efficiency. It is actively assessed and managed during flood events to minimize overtopping risks and downstream impacts.
* Peak flow occurs in April, outside the FIRO-MAR period and during the irrigation season; therefore, limited opportunity for FIRO-MAR to provide any flood risk reduction benefit.

## Slide 16
Intentional Recharge: “Recharge Management Areas”
  In-Basin
  Retention
  Subsidence Prevention
  Disadvantaged Communities
  Groundwater Dependent Ecosystems
Subsidence Prone Areas (>0.15 ft/year)
Disadvantaged Communities (DACs)
GDE-supporting areas
In-basin retention
16
Notes: Recharge for Long-Term Benefit
20-foot depth to groundwater.
1-mile from a connected stream.
Groundwater gradients flow within the watershed / subbasin boundary.
Notes:
Recharge on or near GDEs yielded short-term impacts, while the greatest long-term gains for GDEs came from targeting in-basin retention.

## Slide 17
Intentional Recharge: “Recharge Management Areas”
Stanislaus
Merced
Average Annual Recharge (acre-feet)
Average Annual Recharge (acre-feet)
(Multiple, overlapping RMAs)
Increasing RMA Benefits
Watershed | DACs | All Areas
Calaveras | +6 | +10
Stanislaus | +4 | +2
Tuolumne | +9 | +9
Merced | +13 | +9
USJ | +2 | +4
Average Change in GW Levels (feet)
I-FIRM vs. Baseline – 2050TH
17
Notes: Recharge for Long-Term Benefit
20-foot depth to groundwater.
1-mile from a connected stream.
Groundwater gradients flow within the watershed / subbasin boundary.
Notes:
Recharge on or near GDEs yielded short-term impacts, while the greatest long-term gains for GDEs came from targeting in-basin retention.

## Slide 18
18
“Functional Flows” support ecosystem functions independent of species.
Some watersheds lack key functional flow components in the Baseline.
I-FIRM includes enhanced ecosystem management releases to provide these missing components, partially relying on water stored in the FIRO pool.
Ecosystem Benefits: Applying CEFF
CEFF = California Functional Flows Framework

## Slide 19
19
Diversifying Benefits: Managed Shorebird Habitat
Watershed | Avg. Annual Habitat (acre-days) | Habitat Years (out of 100) | Max Footprint (acres)
Calaveras | 1,599 | 29 | 286
Stanislaus | 794 | 14 | 189
Tuolumne | 10,790 | 46 | 847
Merced | 4,757 | 28 | 444
USJ | 4,200 | 27 | 592
Total | 22,140 | ~28 | 2,358
I-FIRM (2050-TH): FIRO-supported Managed Shorebird Habitat
Notes: California’s Central Valley is an important flyway for migratory birds.
Managed inundation of seasonally flooded wetlands and cropland habitats provides important plant and invertebrate foods for waterbirds during the wintering period.
Increase in the area of managed habitat (particularly winter-flooded croplands and wetlands) is linked to improved body condition, which in turn can influence population demographics
Under the I-FIRM strategy dedicated releases were made from the FIRO-pool at the start of April to parcels suitable for managed shorebird habitat to sustain 2 inches of ponded depth continuously inundated for a minimum of 28 days to allow time for primary and secondary food production to occur.

## Slide 20: Summing Up Flood-MAR Watershed Studies:
I-FIRM shows greatest potential for achieving not only water supply benefits but also reducing flood risk.
Recharge operations can be targeted to share the benefits of improved groundwater conditions more widely.
I-FIRM coordinates ecosystem management with recharge operations to limit impact on habitat and diversify benefits.
Watershed Studies’ reports expected release: Fall 2025!